## Slide 1
Lei Wu
Zhejiang University
Introduction

## Slide 2
Many images and resources used in this lecture are collected from the Internet, and they are used only for the educational purpose. The copyright belong to the original owners, respectively.
Part of slides credit to
  CS 3410: Computer System Organization and Programming (Prof. Weatherspoon, Prof. Bala, Prof. Bracy, and Prof. Sirer @ Cornell)
  Henri Casanova @ Hawaii
  Yajin Zhou, Wenbo Shen @ ZJU
Disclaimer

## Slide 3
Instructors
  沈浩頲 Haoting Shen (htshen@zju.edu.cn)
  卢立 Li Lu (li.lu@zju.edu.cn)
  冯博 Bo Feng (bo.feng@zju.edu.cn)
  吴磊 Lei Wu (lei_wu@zju.edu.cn)
  常瑞 Rui Chang (crix1021@zju.edu.cn)
TAs
  史璐欣
  洪奕迅
Instructor & TA

## Slide 4
Why take computer system courses?
About system courses
Course overview
Evolution of computer systems
Today’s Agenda

## Slide 5: What is a Computer Program?

## Slide 6: Reflect the first Hello World!
About a.out
  Let’s take a look!

## Slide 7: Reflect the first Hello World!
How does it work?
  Why we need to compile the program?
  What is in an executable file?
  How to execute a program?
  What is Operating System (OS)? What does OS do?
  How does the underlying hardware support the software?

## Slide 8: Source Code -> Executable File
int x = 10;
x = 2 * x + 15;
C
compiler
addi r5, r0, 10
muli r5, r5, 2
addi r5, r5, 15
RISC-V
assembly
language
RISC-V
machine
language
assembler
r0 = 0
r5 = r0 + 10
r5 = r5 * 2
r5 = r5 + 15
00000000101000000000001010010011
00000000000100101001001010010011
00000000111100101000001010010011
10 r0 r5 op = addi
15 r5 r5 op = addi
Everything is a number!

## Slide 9: How to Execute Instructions?

## Slide 10
A processor executes instructions
  Processor has some internal state in storage elements (registers)
A memory holds instructions and data
  von Neumann architecture: combined inst and data
A bus connects the two
Basic Computer System

## Slide 11: Von-Neumann
In 1944, John von Neumann joined ENIAC
He wrote a memo about computer architecture, formalizing ENIAC ideas
  Eckert and Mauchly have pretty much been forgotten (they were in the trenches)
These ideas became the Von Neumann architecture model
  A processor that performs operations and controls all that happens
  A memory that contains code and data
  I/O of some kind

## Slide 12: Von-Neumann Model
Amazingly, it’s still possible to think of the computer this way at a conceptual level (model from ~80 years ago!!!)
A computer today has
some differences
CPU
Memory
I/O
System

## Slide 13: Data Stored in Memory
All “information” in the computer is in binary form
  Since Claude Shannon’s M.S. thesis in the 30’s
  0: zero voltage, 1: positive voltage (e.g., 5V)
  bit: the smallest unit of information (0 or 1)
The basic unit of memory is a byte
  1 Byte = 8 bits, e.g., “0101 1101”
Each byte in memory is labeled by a unique address
All addresses in the machine have the same number of bits
  e.g., 64-bit addresses on ARM64
The processor has instructions that say “Read the byte at address X and give me its value” and “Write some value into the byte at address X”

## Slide 14: Conceptual View of Memory
address | content
0000 0000 0000 0000 | 0110 1110
0000 0000 0000 0001 | 1111 0100
0000 0000 0000 0010 | 0000 0000
0000 0000 0000 0011 | 0000 0000
0000 0000 0000 0100 | 0101 1110
0000 0000 0000 0101 | 1010 1101
0000 0000 0000 0110 | 0000 0001
0000 0000 0000 0111 | 0100 0000
0000 0000 0000 1000 | 1111 0101
... | ...

## Slide 15: Conceptual View of Memory
address | content
0000 0000 0000 0000 | 0110 1110
0000 0000 0000 0001 | 1111 0100
0000 0000 0000 0010 | 0000 0000
0000 0000 0000 0011 | 0000 0000
0000 0000 0000 0100 | 0101 1110
0000 0000 0000 0101 | 1010 1101
0000 0000 0000 0110 | 0000 0001
0000 0000 0000 0111 | 0100 0000
0000 0000 0000 1000 | 1111 0101
... | ...
At address 0000 0000 0000 0010
the content is 0000 0000

## Slide 16: Conceptual View of Memory
address | content
0000 0000 0000 0000 | 0110 1110
0000 0000 0000 0001 | 1111 0100
0000 0000 0000 0010 | 0000 0000
0000 0000 0000 0011 | 0000 0000
0000 0000 0000 0100 | 0101 1110
0000 0000 0000 0101 | 1010 1101
0000 0000 0000 0110 | 0000 0001
0000 0000 0000 0111 | 0100 0000
0000 0000 0000 1000 | 1111 0101
... | ...
At address 0000 0000 0000 0100
the content is 0101 1110

## Slide 17: Both Code and Data in Memory
Once a program is loaded in memory, its address space contains both code and data
To the CPU those are not really different, but the programmer knows which bytes are data and which are code
  Always conveniently hidden from you if you’ve never written assembly
  But we’ll have to keep code/data straight in these lecture notes
Memory
0010 0001
0000 1110
1111 0000
1000 0000
...
...
Address
Value
0000 1100
0010 1101
0000 1101
1111 0010
0101 1111
1111 0010
...
...
Code
Data
Example Address Space

## Slide 18: Memory Layout

## Slide 19: We need a CPU
So now we have a memory in which we can store/retrieve bytes at precise location
These bytes presumably have some useful meaning to us
  e.g., integers, ASCII codes of characters, floating points numbers, RGB values
  e.g., instructions that specify what to do with the data; when you buy a processor, the vendor defines the instruction set (e.g., instruction “0010 1101” means “increment some useful counter”)
The CPU is the piece of hardware that modifies the content of memory
  In fact, one can really think of the CPU as a device that moves one memory state (i.e., all the stored content) to another memory state (some new, desired stored content)

## Slide 20: What’s in the CPU?
Memory
I/O
System
CPU

## Slide 21
Memory
I/O
System
Control
Unit
ALU
Program counter
register
register
register
current instruction
What’s in the CPU?

## Slide 22: What’s in the CPU?
Control
Unit
ALU
Program counter
register
register
register
Registers: the “variables” that hardware instructions work with
Data can be loaded from memory into a register
Data can be stored from a register back into memory
Operands and results of computations are in registers
Accessing a register is really fast
There is a limited number of registers
current instruction

## Slide 23: What’s in the CPU?
Control
Unit
ALU
Program counter
register
register
register
Arithmetic and Logic Unit: what you do computation with
Used to compute a value based on current register values and
store the result back into a register
+, *, /, -, OR, AND, XOR, etc.
current instruction

## Slide 24: What’s in the CPU?
Control
Unit
ALU
Program counter
register
register
register
Program Counter: Points to the next instruction
Special register that contains the address in memory of the next instruction that should be executed
(gets incremented after each instruction, or can be set to whatever value whenever there is a change of control flow)
current instruction

## Slide 25: What’s in the CPU?
Control
Unit
ALU
Program counter
register
register
register
Current Instruction: Holds the instruction that’s currently being executed
current instruction

## Slide 26: What’s in the CPU?
Control
Unit
ALU
Program counter
register
register
register
Control Unit: Decodes instructions and make them happen
Logic hardware that decodes instructions (i.e., based on their bits) and sends the appropriate (electrical) signals to hardware components in the CPU
current instruction

## Slide 27: The CPU in its “Glory”

## Slide 28
Basic knowledge needed for many other areas of CS
  Compiler
  Parallel Computing
  New era of AI/ML
Understand where the world is going
  Delve into the underlying implementation
  Address bug or performance issues
  Become more effective programmers
Why Take System Courses?
The Mysteries of Computing will be revealed!

## Slide 29
Why take system courses?
About system courses
Course overview
Evolution of computer systems
Today’s Agenda

## Slide 30: A Look into AMD CPU

## Slide 34: A Look into AMD CPU

## Slide 35
Transistor Schematic
Full adder
Very Large Scale Integrated (VLSI) Circuit

## Slide 36
Layout

## Slide 37: Layer of Abstraction

## Slide 38: Abstract Layers of A COMPUTER SYSTEM
Application
Compiler / Libraries of Macros and Procedures
Operating System (OS)
Instruction Set Architecture (ISA)
Computer Organization (Micro Architecture)
Register Transfer Level (RTL)
Digital Logic Circuit (DLC)
Device Technology
Software
Hardware
Operating System
Computer Architecture
Computer Organization
Digital Logic

## Slide 39: Covered in ZJU Computer System Courses
Application
Compiler / Libraries of Macros and Procedures
Operating System (OS)
Instruction Set Architecture (ISA)
Computer Organization (Micro Architecture)
Register Transfer Level (RTL)
Digital Logic Circuit (DLC)
Device Technology
Software
Hardware
System-II&III
System-I

## Slide 40: ZJU Computer System Courses - since 2021
System I
System II
System III
Digital Logic
Computer Organization
Operating System
Computer Architecture
Notes: Add security

## Slide 41: ZJU Computer System Courses - since 2021

## Slide 42: ZJU Computer System Courses - since 2021

## Slide 43: ZJU Computer System Courses - since 2021

## Slide 44: Experiments for Computer System

## Slide 45: Experiments for Computer System

## Slide 46: Experiments for Computer System

## Slide 47: ZJU Computer System Courses
System I
System II
System III
Digital Logic
Computer Organization
Operating System
Computer Architecture
System Security
YOUR OWN CPU!
YOUR FIRST KERNEL based on YOUR OWN CPU!
YOUR ADVANCED KERNEL based on YOUR OWN CPU!
47
Notes: Add security

## Slide 48: ZJV 1.0 技术指标——微结构设计
What is more? Your own CPU.
48

## Slide 49
ZJV 1.0 技术指标——微结构设计
What is more? Your own CPU.
49

## Slide 50: ZJV1.0——流片成果（一生一芯二期）
50

## Slide 51
What is more? Your own CPU.
51

## Slide 52
操作系统移植
  支持pmon的全部指令运行
  支持ucore的运行
  完成Linux的启动流程到用户态
  自主搭建的差分测试框架dtqemu
    模拟RAM和串口等外设
    同步中断
    比对qemu和AMipsel的寄存器
  便捷Linux的调试
What is more? Your own CPU.
52

## Slide 53: ZJV2.0 ——流片成果（一生一芯三期）
53

## Slide 54
What is more? Your own CPU + system.
逐梦杯总决赛：
自主设计优化，获得1789性能分
面向通用系统，启动Linux 发行版
着眼安全特性，保护数据完整性和机密性
54

## Slide 55
What is more? Your own CPU + system.

## Slide 56
ZJV 1.0
ZJV 2.0
2020.12
第一次投片
2021.08
龙芯杯一等奖
（性能第一名）
Amipsel
待续
2021.12
ZJV 2.0投片
ZJV 1.0第二次投片
ZJV 2.0
plus
2022
逐梦杯
冠军
MMM
2022.08
龙芯杯二等奖
（性能第一名）
What is more? Our idea (not only CPU)
ZJV = ZheJiang University + RISC-V

## Slide 57
浙江大学信息安全专业
第一届计算机系统贯通课程

## Slide 58
浙江大学信息安全专业
第二届计算机系统贯通课程

## Slide 59
Why take system courses?
About system courses
Course overview
Evolution of computer systems
Today’s Agenda

## Slide 60: Course Objective
Understand the HW / SW interface
  How a processor works
  How a computer is organized
Establish a foundation for building applications
  How to write a good program
    Good = correct, fast, and secure
  How to understand where the world is going
Understand technology (past, present, future)

## Slide 61: Course Topics
Information Representation ~ 2 weeks
Foundations of Digital Logic ~ 1 week
Combinational Logic Circuit ~ 1 week
Sequential Logic Circuit ~ 2 week
Computational Operations & Units ~ 1 week
Assembly Language ~ 1 weeks
Instruction Set Architecture (ISA) ~ 2 weeks
Single-Cycle CPU Design ~ 6 weeks

## Slide 62: Don’t Worry, Just A Small Target……
Memory
I/O
System
Control
Unit
ALU
Program counter
register
register
register
current instruction

## Slide 63: Prerequisites
Courses
  C Programming Language - required
  Assembly Language - optional
Skills
  Basic programming experience
  The more, the better

## Slide 64: Course Material
Lecture Notes
  Will be posted
Textbook
  Logic and Computer Design Fundamentals
    Fifth Edition
References
  《数字逻辑与计算机组成》
    编者：袁春风、武港山、吴海军、余子濠
  Computer Organization and Design
    RISC-V Edition 1st Edition

## Slide 65: Some Other References (Optional)

## Slide 66: C Resources (Optional)

## Slide 67: Course Organization
Lectures
  Monday (ZJG East 1A-214)
    7-8 (14:15 – 15:50 )
  Wednesday (ZJG East 1A-214)
    7-8 (14:15 – 15:50 )
Labs
  Thursday (ZJG East 4-509)
    6-8 (13:25 AM – 15:50 AM)
  No group, please work alone

## Slide 68: Class Grading

## Slide 69: A Look into AMD CPU

## Slide 70: LUT

## Slide 71: LUT

## Slide 72: Course Policies
Academic integrity
  We will strictly enforce the university, college, and department policies against academic dishonesty
  Plagiarism in any form will not be tolerated!
Unless otherwise noted, work turned in should reflect your independent capabilities
  If unsure, note / cite sources and help
Late penalized: homework 5%/day，project 25%/week
  No penalty for documented emergency or by prior arrangement in special circumstances

## Slide 73
Why take system courses?
About system courses
Course overview
Evolution of computer systems
Today’s Agenda

## Slide 74
Evolution of Computer Systems

## Slide 76
Primal Ancient

## Slide 77
Alan Turing
Turing Machine
1936
= abstract model for CPU that can simulate any algorithm
Ancient
Notes: How does The Imitation Game, Engima/Bombe, Turing relate to you and this course?!
Alan Turing thesis in 1936 came up with an abstract model for a CPU that can simulate any algorithm, a Turing Machine. You will build a CPU and understand it and its organization
http://en.wikipedia.org/wiki/Turing_machine
A Turing machine is a hypothetical device that manipulates symbols on a strip of tape according to a table of rules. Despite its simplicity, a Turing machine can be adapted to simulate the logic of any computer algorithm, and is particularly useful in explaining the functions of a CPU inside a computer.
Note that every part of the machine (i.e. its state, symbol-collections, and used tape at any given time) and its actions (such as printing, erasing and tape motion) is finite, discrete and distinguishable; it is the unlimited amount of tape and runtime that gives it an unbounded amount of storage space.

## Slide 78
In the Ancient Days…
The Bombe
used by the Allies to
break the German
Enigma machine during
World War II
Enigma machine
Used by the Germans during
World War II to encrypt and
exchange secret messages
Notes: http://en.wikipedia.org/wiki/Bombe
How many possible combinations to break an Enigma cipher text (msg encrypted by the Enigma machine)?
Rotors x Rotor posititions x plugboard combinations with 10 pairs = 159 quintillion = 1.59 x 10^20 158,962,555,217,826,360,000
Rotors (3 of 5 rotors): 5 x 4 x 3 = 60
Rotor positions: 26 x 26 x 26 = 17,526
plugboard: 26! / (6!10!2^10)
Numberphile on Enigma/Bombe
For those who want to learn more about the mechanism of the Bombe and how it exploited the flaw in the Enigma, Numberphile has recently done an excellent episode on it. Enjoy!
Flaw in the Enigma: http://www.youtube.com/watch?v=V4V2bpZlqx8
Previous episode on Enigma: http://www.youtube.com/watch?v=G2_Q9FoD-oQ

## Slide 79
First Generation
ENIAC Electronic Numerical Integrator And Computer
1946
John Mauchly
J. Presper Eckert

## Slide 80
Second Generation
IBM 7090 Human Computers programming the IBM 7090
Mary Jackson
Hidden Figures

## Slide 81
Generations of Computer Systems

## Slide 82
Vacuum Tube -> Transistor

## Slide 83
Where did it begin?
Electrical Switch
  On/Off
  Binary
Transistor
The first transistor on a workbench at AT&T Bell Labs in 1947

## Slide 84
Then and Now
https://www.computershopper.com/computex-2015/performance-preview-desktop-broadwell-at-computex-2015
https://en.wikipedia.org/wiki/Transistor_count
The first transistor
  One workbench at AT&T Bell Labs
  1947
  Bardeen, Brattain, and Shockley
Intel Broadwell
  7.2 billion transistors, 14nm
  456 square millimeters
  Up to 22 processing cores
https://en.wikipedia.org/wiki/Transistor_count

## Slide 85
Moore’s Law
1965
  # of transistors integrated on a die doubles every 18-24 months (i.e., grows exponentially with time)
Amazingly visionary
  2300 transistors, 1 MHz clock (Intel 4004) - 1971
  16 Million transistors (Ultra Sparc III)
  42 Million transistors, 2 GHz clock (Intel Xeon) – 2001
  55 Million transistors, 3 GHz, 130nm technology, 250mm2 die (Intel Pentium 4) – 2004
  290+ Million transistors, 3 GHz (Intel Core 2 Duo) – 2007
  721 Million transistors, 2 GHz (Nehalem) - 2009
  1.4 Billion transistors, 3.4 GHz Intel Haswell (Quad core) – 2013
  7.2 Billion transistors, 3-3.9 GHz Intel Broadwell (22-core) – 2016
  …

## Slide 87
Thanks!