## Slide 1
Lei Wu
Zhejiang University

## Slide 2
Many images and resources used in this lecture are collected from the Internet, and they are used only for the educational purpose. The copyright belong to the original owners, respectively.
Part of slides credit to
  CSAPP @ CMU
  Prof. Yabo Dong @ ZJU
Disclaimer

## Slide 3: Overview
Introduction to computer systems
Binary number representation
Arithmetic operations
Representation of numeric data
Representation of non-numeric data
Data width and storage

## Slide 4: Numeric Data
Primitive types
Numeric
Non-numeric
Integer number
(fixed-point)
Real number
(floating-point)
Unsigned
Signed
Bits
Character/
String
Low-level programmer’s/
hardware system designer’s perspective
Notes: 机器语言只有最基本的数据类型：
1）数值型数据：表示数量的多少，可比较大小。具体而言，整数（无符号，有符号）用定点数表示，以及实数用浮点数表示。
2）非数值型数据：字符和逻辑值。

## Slide 5: Elements to Represent Numerical Data
Carry counting system
Number representation
  Fixed-point vs. floating-point
Encoding method
Notes: 数值型数据表示的三要素
整数小数点固定，实数不固定。

## Slide 6: Representation of Numeric Data
Fixed-point number representation
Representation of integers
Floating-point number representation
Binary codes for decimal digits

## Slide 7: Representation of Numeric Data
Fixed-point number representation
Representation of integers
Floating-point number representation
Binary codes for decimal digits

## Slide 8: Fixed-point Number Representation
The number represented by the computer‘s internal code is called machine number, and the corresponding value is called true value.
After encoding XT with n-bit binary numbers, the machine number X can be expressed as:
Unsigned integer
  0≤X ≤ 2n-1
Signed integer
  Depend on the encoding method
Notes: 计算机内部编码表示后的数叫做机器数，机器数真正的值称为真值。
数值型数据在计算机内部的编码问题，本质上是机器数X的各位Xi的取值和真值XT的关系问题。
True value: -10
Machine number: -1010B -> 11110110B

## Slide 9: Encoding Methods
Original code
Complement code
Inverse code
Frameshift code
Notes: 整数小数点固定，实数不固定。

## Slide 10: Original Code
The original code representation of a number consists of the sign bit followed by the value bit, also known as sign-and-magnitude representation.
A positive number and the corresponding negative number share the same value part
  The conversion between the original code and true value is straightforward, i.e., just alter the sign bit
The coding rules are as follows:
  XT > 0, Xn-1 = 0, Xi = Xi’ (0≤i ≤ n-2)
  XT < 0, Xn-1 = 1, Xi = Xi’ (0≤i ≤ n-2)
There are two ways to represent 0!
Notes: 原码表示由符号位后直接跟数值位构成，又称为符号-数值表示法。
[+0] = 0 000…0
[-0] = 1 000…0
True value: -10
Machine number: -1010B -> 10001010B
缺点：1）0不唯一；2）符号和数值部分必须分开处理。

## Slide 11: Complement Code
Aka two's complement
The complement representation is composed of the sign bit followed by the modulus 2n complement of the truth value.
Implement subtraction with addition

## Slide 12: The Modulo Operation
If A, B, M satisfy A = B + K * M, then recorded as A ≡ B(mod M), call B and A congruence modulo M.
The clock is a typical modular arithmetic system with a modulus of 12.
Assuming that the hand of the clock is now pointing to 10 o'clock, to set it to 6 o'clock, there are the following two dialing methods.
  Dial four counterclockwise (10 – 4 = 6)
  Dial eight clockwise (10 + 8 = 18 ≡ 6 (mod 12))
Notes: A和B除以M后余数相同，即B和A为模M同余。
10-4 ≡ 10 + (12 – 4) ≡ 10 + 8 (mod 12)，即-4 ≡ 8 (mod 12)
-4和8对模12同余，换言之，8是-4对模12的补码。
为什么可以用加法实现减法？
对某个确定的模，A减去小于模的另一个数B，可以用A加上-B的补码来代替。
8 -2 = 8 + (12 – 2) (mod 12)= 6

## Slide 13: Results of the Modulo Operation
Limited (n) bits of a computer system
  Modulo is 2n
The calculation of two n-bit numbers may lead to a number with more than n bits (n+1), and the highest n+1 bit needs to be discarded.
As a result, there exist two cases
  The n bits cannot represent the result correctly
    Overflow
  The n bits can represent the result correctly
    The highest n+1 bit does not affect the calculation result
Notes: 1）n位数无法正确表示运算结果：即溢出，比如两个同号数相加，和超出了n位数可表示范围
2）n位数能够正确表示运算结果：高位舍去不影响结果，如两个同号数相减或者两个异号数相加；舍去高位的操作等价于将一个多余n位的数除以2^n，保留余数作为结果。

## Slide 14: Definition of Complement Code
The complement symbol of a positive number is 0, and the value part is itself; the complement of a negative number is equal to the difference between the modulus and the absolute value of the negative number.
The coding rules are as follows:
For any XT, its complement is [XT]C = M + XT (mod M)

## Slide 15: The Complement Code for the Binary Number with N Bits
N-bit binary number
  One bit for sign and n-1 bits for value
  [XT]C = 2n + XT (-2n-1 ≤ XT<2n-1, mod 2n)
The complements of some special numbers
  0
  -1
  2n-1
  -2n-1
The Number of Bits Are Important!
  -2n-1 's complement representation might be different for different bits (n vs. n+1)
Notes: -2n-1<= XT < 2n-1
左边小于等于，右边小于
e.g., n = 4 and n = 5

## Slide 16: The Conversion Between Complement Code and True Value
True value -> complement code
  Positive number
    The sign bit is 0
    The value part does not need to be changed
  Negative number
    The sign bit is 1
    Invert the bits of value part, and add 1 to the result
Complement code -> true value
  The sign bit is 0
    Positive number
    The value part does not need to be changed
  The sign bit is 1
    Negative number
    Invert the bits of value part, and add 1 to the result
What about [XT]C -> [-XT]C ?
Notes: 8 bits
[110 1100]C = 28 + 110 1100 = 1 0000 0000 + 110 1100 (mod 28) = 0110 1100
[-110 1100]C = 28 - 110 1100 = 1 0000 0000 - 110 1100 (mod 28) = 1001 0100
求补码：对于正数，符号位为0，其余同真值各位；对于负数，符号位取1，数值部分取反加1得到。
[-110 0011]C = 1 001 1100 + 0 000 0001 = 1 001 1101
补码求真值，符号位为0，则真值符号为正，数值部分不变；符号位为1，则真值符号为负，数值部分由补码取反-1得到。
1 011 0100 = -(100 1011 + 1) = -100 1100
根据补码[XT]C求[-XT]C的方法是，对[XT]C各位取反加1，最小负数取负后会溢出。
The range will be
-2n-1 ≤X ≤ 2n-1-1 (compare with unsigned integer, 0≤X ≤ 2n-1)
Be careful about the potential overflow!

## Slide 17: Shortcuts and Advantages of Complement Code
Useful shortcuts
  Negation shortcut
    Invert every 0 to 1 and every 1 to 0, then add one to the result
  Sign extension shortcut
    Extend the sign bit by replicating it to fill the new bits
Advantages (vs. sign-and-magnitude)
  No +0 and -0 anymore
  Hardware simplicity
    Only needs to test only the sign bit to determine if a number is positive or negative.
Notes: 8 bits
[110 1100]C = 28 + 110 1100 = 1 0000 0000 + 110 1100 (mod 28) = 0110 1100
[-110 1100]C = 28 - 110 1100 = 1 0000 0000 - 110 1100 (mod 28) = 1001 0100
求补码：对于正数，符号位为0，其余同真值；对于负数，符号位取1，数值部分取反加1得到。
[-110 0011]C = 1 001 1100 + 0 000 0001 = 1 001 1101
根据补码[XT]C求[-XT]C的方法是，对[XT]C各位取反加1，最小负数取负后会溢出。
The range will be
-2n-1 ≤X ≤ 2n-1-1 (compare with unsigned integer, 0≤X ≤ 2n-1)
Be careful about the potential overflow!

## Slide 18: Deformation Complement
In order to determine whether the result of the operation overflows, there is a two-symbol-bit complement representation, which is called deformation complement (modulo 4 complement).
In the double sign bit, the left bit is the real sign bit, and the right bit is used to determine whether the overflow occurs.
The representation of the deformation complement
Notes: XT = -1011
6 bits: [XT]DC= 26 – 1011 = 100 0000 – 00 1011 = 11 0101
8 bits: [XT]DC= 28 – 1011 = 1 0000 0000 – 0000 1011 = 1111 0101

## Slide 19: Inverse Code
Aka one's complement
The difference with the complement
  Just invert, no add
There are two ways to represent 0
Less range
Complicated calculation
  End-around carry/borrow
Notes: 循环进/借位
（-1）+ 2
1110 -1
+ 0010 2
=========== ====
1 0000 0 —An end-around carry is produced, and the sign bit of the intermediate result is 0.
+ 0001 1 —Add the end-around carry from the result.
=========== ====
0001 1 —The correct result (2 − 1 = 1)
-1 + (-3)
1110 -1
+ 1100 -3
=========== ====
1 1010 -5
+ 0001 1
=========== ====
1011 -4 —The correct result

## Slide 20: Frameshift Code
Be used to represent the exponent part of a floating-point number
A floating-point number is represented by two fixed-point numbers with a sign bit
  A fixed-point decimal is used to represent the significand of the floating-point number
  A fixed-point integer is used to represent the order of power of two of the floating-point number
Will discuss it later
s | exp | frac

## Slide 21: Representation of Numeric Data
Fixed-point number representation
Representation of integers
Floating-point number representation
Binary codes for decimal digits

## Slide 22: Not That Trivial to Represent Integers
Unsigned integers vs. signed integers
  Range of an 8-bit unsigned number is 0 ~ (28 - 1)
  Range of an 8-bit signed number is -27~ (27 - 1)
Conversion between unsigned integers and signed integers is allowed in C language
  The machine code before and after the conversion is unchanged
  The interpretation before and after the conversion has changed
  May lead to unexpected effects!
Notes: C语言规定，无符号整数与带符号整数同时参与运算，统一按无符号整数进行运算。
-2147483648 < 2147483647 in C90 and C99
1000 0000 0000 0000 0000 0000 0000 0000
0111 1111 1111 1111 1111 1111 1111 1111
2147483648 is regarded as an unsigned integer in C90, and as a signed integer in C99.
2147483647 is a signed integer in both cases.
=> In C90, the result is False; in C99, the result is True.

## Slide 23: Representation of Integers
Bit-level manipulations in C
Representation: unsigned and signed
Conversion, casting
Expanding, truncating
Addition, negation, multiplication, shifting
Summary

## Slide 24: Bit-Level Operations in C
Operations &, |, ~, ^ Available in C
  Apply to any “integral” data type
    long, int, short, char, unsigned
  View arguments as bit vectors
  Arguments applied bit-wise
Examples (Char data type)
  ~0x41 -> 0xBE
    ~010000012 -> 101111102
  ~0x00 -> 0xFF
    ~000000002 -> 111111112
  0x69 & 0x55 -> 0x41
    011010012 & 010101012 -> 010000012
  0x69 | 0x55 -> 0x7D
    011010012 | 010101012 -> 011111012
Notes: C语言中的位运算： &, |, ~, ^
  适用于任何整型数据类型：long, int, short, char, unsigned
  将操作数视为位向量
  将参数按位运算
按位异或是一种加的形式
A ^ A = 0
int inplace_swap(int *x, int *y)
{
*x = *x ^ *y; /* #1 */
*y = *x ^ *y; /* #2 */
*x = *x ^ *y; /* #3 */
}
A -> A^B -> A^B -> (A^B)^A = (B^A)^A = B^(A^A) = B^0 = B -> B
B -> B -> (A^B)^B = A^(B^B) = A^0 = A -> A -> A

## Slide 25: Contrast: Logic Operations in C
Contrast to Logical Operators
  &&, ||, !
    View 0 as “False”
    Anything nonzero as “True”
    Always return 0 or 1
    Early termination (short cut)
Examples (char data type)
  !0x41 -> 0x00
  !0x00 -> 0x01
  !!0x41 -> 0x01
  0x69 && 0x55 -> 0x01
  0x69 || 0x55 -> 0x01
  p && *p (avoids null pointer access)

## Slide 26: Shift Operations
Left Shift: x << y
  Shift bit-vector x left y positions
      Throw away extra bits on left
    Fill with 0’s on right
Right Shift: x >> y
  Shift bit-vector x right y positions
    Throw away extra bits on right
  Logical shift
    Fill with 0’s on left
  Arithmetic shift
    Replicate most significant bit on right
Undefined Behavior
  Shift amount < 0 or ≥ word size
01100010
Argument x
00010000
<< 3
00011000
Log. >> 2
00011000
Arith. >> 2
10100010
Argument x
00010000
<< 3
00101000
Log. >> 2
11101000
Arith. >> 2
00010000
00010000
00011000
00011000
00011000
00011000
00010000
00101000
11101000
00010000
00101000
11101000
Notes: 左移: x << y
  将位向量x向左移动 y位
    扔掉左边多出(移出)的位
    在右边补0
右移: x >> y
  将位向量x向右移动 y位
    扔掉右边多出(移出)的位
  逻辑(无符号数)右移：在左边补0
  算术右移：复制左边的最高位(y次)
未明确定义
  移位数量y< 0 或 y ≥ x的字长(位数)

## Slide 27: Some Useful Terminology
Notes: Terminology for integer data and arithmetic operations. The subscript w denotes the number of bits in the data representation.

## Slide 28: Encoding Integers
short int x = 15213;
short int y = -15213;
C short 2 bytes long
Sign Bit
  For 2’s complement, most significant bit indicates sign
    0 for nonnegative
    1 for negative
Unsigned
Two’s Complement
Sign
Bit
Notes: 符号位
  对于补码(2’s complement), 最高位表示符号
    0 表示非负数（ != 正数），1 表示负数

## Slide 29: Encoding Example (Cont.)
x = 15213: 00111011 01101101
y = -15213: 11000100 10010011

## Slide 30: Numeric Ranges
Unsigned Values
  UMin = 0
    000…0
  UMax = 2w – 1
    111…1
Two’s Complement Values
  TMin = –2w–1
    100…0
  TMax = 2w–1 – 1
    011…1
Other Values
  Minus 1
    111…1
Values for W = 16

## Slide 31: Values for Different Word Sizes
Observations
  |TMin | = TMax + 1
    Asymmetric range
  UMax = 2 * TMax + 1
C Programming
  #include <limits.h>
    #define INT_MAX 2147483647
    #define INT_MIN (-INT_MAX-1)
    #define UINT_MAX 0xffffffff
  Values platform specific
    #define ULONG_MAX
    #define LONG_MAX
    #define LONG_MIN (-LONG_MAX-1)

## Slide 32: Unsigned & Signed Numeric Values
Equivalence
  Same encodings for nonnegative values
Uniqueness
  Every bit pattern represents unique integer value
  Each representable integer has unique bit encoding
 Can Invert Mappings
  U2B(x) = B2U-1(x)
    Bit pattern for unsigned integer
  T2B(x) = B2T-1(x)
    Bit pattern for two’s comp integer
X
B2T(X)
B2U(X)
0000
0
0001
1
0010
2
0011
3
0100
4
0101
5
0110
6
0111
7
–8
8
–7
9
–6
10
–5
11
–4
12
–3
13
–2
14
–1
15
1000
1001
1010
1011
1100
1101
1110
1111
0
1
2
3
4
5
6
7
Notes: 相同
  非负数值的编码相同
单值性
  每个位模式对应一个唯一的整数值
  每个可描述整数有一个唯一编码
 有逆映射
  U2B(x) = B2U-1(x)
    无符号整数的位模式
  T2B(x) = B2T-1(x)
    补码的位模式

## Slide 33: Mapping Between Signed & Unsigned
T2U
T2B
B2U
Two’s Complement
Unsigned
Maintain Same Bit Pattern
x
ux
X
U2T
U2B
B2T
Two’s Complement
Unsigned
Maintain Same Bit Pattern
ux
x
X
Mappings between unsigned and two’s complement numbers: keep bit representations and reinterpret
Notes: 有符号数和无符号数转换规则: 位模式不变、数值可能改变(按不同编码规则重新解读)

## Slide 34: Mapping Signed  Unsigned
Signed
0
1
2
3
4
5
6
7
-8
-7
-6
-5
-4
-3
-2
-1
Unsigned
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Bits
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
1101
1110
1111
=
+/- 16
U2T
T2U

## Slide 35: Relation between Signed & Unsigned
+
+
+
+
+
+
• • •
-
+
+
+
+
+
• • •
ux
x
w–1
0
Large negative weight
becomes
Large positive weight
T2U
T2B
B2U
Two’s Complement
Unsigned
Maintain Same Bit Pattern
x
ux
X
Notes: 大的负权值
变为
大的正权值

## Slide 36: Conversion Visualized
0
TMax
TMin
–1
–2
0
UMax
UMax – 1
TMax
TMax + 1
2’s Complement Range
Unsigned
Range
2’s Comp.  Unsigned
  Ordering Inversion
  Negative  Big Positive
Notes: 补码 无符号数
  顺序倒置
  负数  大整数

## Slide 37: Signed vs. Unsigned in C
Constants
  By default are considered to be signed integers
  Unsigned if have “U” as suffix
    0U, 4294967259U
Casting
  Explicit casting between signed & unsigned same as U2T and T2U
    int tx, ty;
    unsigned ux, uy;
    tx = (int) ux;
    uy = (unsigned) ty;
  Implicit casting also occurs via assignments and procedure calls
    tx = ux;
    uy = ty;
Notes: 常量
  数字默认是有符号数
  无符号数用后缀 “U”
    0U, 4294967259U
类型转换
  显示的强制类型转换
    int tx, ty;
    unsigned ux, uy;
    tx = (int) ux;
    uy = (unsigned) ty;
  隐式的类型转换（赋值、函数调用等情况下发生）
    tx = ux;
    uy = ty;

## Slide 38: Casting Surprises
  0 0U == unsigned
  -1 0 < signed
  -1 0U > unsigned
  2147483647 -2147483648 > signed
  2147483647U -2147483648 < unsigned
  -1 -2 > signed
  (unsigned) -1 -2 > unsigned
  2147483647 2147483648U < unsigned
  2147483647 (int) 2147483648U > signed
Expression Evaluation
  If there is a mix of unsigned and signed in single expression, signed values implicitly cast to unsigned
  Including comparison operations <, >, ==, <=, >=
  Examples for W = 32: TMIN = -2,147,483,648 , TMAX = 2,147,483,647
Constant1 Constant2 Relation Evaluation
  0 0U
  -1 0
  -1 0U
  2147483647 -2147483647-1
  2147483647U -2147483647-1
  -1 -2
  (unsigned)-1 -2
  2147483647 2147483648U
  2147483647 (int) 2147483648U
Notes: 表达式计算
  表达式中有符号和无符号数混用时：
  有符号数隐式转换为无符号数
  包括比较运算符 <, >, ==, <=, >=
  例如W = 32:
  TMIN = -2,147,483,648
  TMAX =2,147,483,647

## Slide 39: Code Security Example
Similar to code found in FreeBSD’s implementation of getpeername
There are legions of smart people trying to find vulnerabilities in programs
/* Kernel memory region holding user-accessible data */
#define KSIZE 1024
char kbuf[KSIZE];
/* Copy at most maxlen bytes from kernel region to user buffer */
int copy_from_kernel(void *user_dest, int maxlen) {
/* Byte count len is minimum of buffer size and maxlen */
int len = KSIZE < maxlen ? KSIZE : maxlen;
memcpy(user_dest, kbuf, len);
return len;
}

## Slide 40: Typical Usage
/* Kernel memory region holding user-accessible data */
#define KSIZE 1024
char kbuf[KSIZE];
/* Copy at most maxlen bytes from kernel region to user buffer */
int copy_from_kernel(void *user_dest, int maxlen) {
/* Byte count len is minimum of buffer size and maxlen */
int len = KSIZE < maxlen ? KSIZE : maxlen;
memcpy(user_dest, kbuf, len);
return len;
}
#define MSIZE 528
void getstuff() {
char mybuf[MSIZE];
copy_from_kernel(mybuf, MSIZE);
printf(“%s\n”, mybuf);
}

## Slide 41: Malicious Usage
/* Kernel memory region holding user-accessible data */
#define KSIZE 1024
char kbuf[KSIZE];
/* Copy at most maxlen bytes from kernel region to user buffer */
int copy_from_kernel(void *user_dest, int maxlen) {
/* Byte count len is minimum of buffer size and maxlen */
int len = KSIZE < maxlen ? KSIZE : maxlen;
memcpy(user_dest, kbuf, len);
return len;
}
#define MSIZE 528
void getstuff() {
char mybuf[MSIZE];
copy_from_kernel(mybuf, -MSIZE);
printf(“%s\n”, mybuf);
}
/* Declaration of library function memcpy */
void *memcpy(void *dest, void *src, size_t n);
size_t int copy_from_kernel(void *user_dest, size_t maxlen)

## Slide 42: Summary Casting Signed ↔ Unsigned: Basic Rules
Bit pattern is maintained
But reinterpreted
Can have unexpected effects: adding or subtracting 2w
Expression containing signed and unsigned int
  int is cast to unsigned!!
Notes: 位模式不变
重新解读（按目标编码类型的规则解读）
会有意外副作用: 数值被 +或- 2w
表达式含无符号数和有符号数时
  有符号数被转换成无符号数（如int 转成unsigned int）
  当心副作用！！！

## Slide 43: Sign Extension
Task:
  Given w-bit signed integer x
  Convert it to w+k-bit integer with same value
Rule:
  Make k copies of sign bit:
  X  = xw–1 ,…, xw–1 , xw–1 , xw–2 ,…, x0
k copies of MSB
• • •
X
X 
• • •
• • •
• • •
w
w
k

## Slide 44: Sign Extension Example
Converting from smaller to larger integer data type
C automatically performs sign extension
short int x = 15213;
int ix = (int) x;
short int y = -15213;
int iy = (int) y;
Decimal
Hex
Binary
x
15213
3B 6D
00111011 01101101
ix
15213
00 00 3B 6D
00000000 00000000 00111011 01101101
y
-15213
C4 93
11000100 10010011
iy
-15213
FF FF C4 93
11111111 11111111 11000100 10010011
Notes: 从短整数类型向长整数类型转换时，C自动进行符号扩展

## Slide 45: Summary: Expanding, Truncating: Basic Rules
Expanding (e.g., short int to int)
  Unsigned: zeros added
  Signed: sign extension
  Both yield expected result
Truncating (e.g., unsigned to unsigned short)
  Unsigned/signed: bits are truncated
  Result reinterpreted
  Unsigned: mod operation
  Signed: similar to mod
  For small numbers yields expected behavior
Notes: 扩展 (例如从short int 到int的转换)
  无符号数: 填充0
  有符号数:符号扩展
  结果都是明确的预期值
截断 (例如从unsigned 到unsigned short的转换)
  无论有/无符号数:多出的位（高位）均被截断
  结果重新解读
  无符号数: 相当于求模运算
  有符号数: 与求模运算相似
  对于小整数，结果是明确（正确）的预期值

## Slide 46: Negation: Complement & Increment
Claim: Following Holds for 2’s Complement
  ~x + 1 == -x
Complement
  Observation: ~x + x == 1111…111 == -1
Complete Proof?
1
0
0
1
0
1
1
1
x
0
1
1
0
1
0
0
0
~x
+
1
1
1
1
1
1
1
1
-1
Notes: n bits
[x]C = 2n + x (mod 2n)
[-x]C = 2n - x (mod 2n)
= 2n-1 + 2n-1 – x (mod 2n)
= 2n-1 + (2n-1 – 1 – x) + 1 (mod 2n)
=> sign bit + x inverted + 1

## Slide 47: Complement & Increment Examples
x = 15213
x = 0

## Slide 48: Unsigned Addition
Standard Addition Function
  Ignores carry output
Implements Modular Arithmetic
  s = UAddw(u , v) = u + v mod 2w
• • •
• • •
u
v
+
• • •
u + v
• • •
True Sum: w+1 bits
Operands: w bits
Discard Carry: w bits
UAddw(u , v)
Notes: 标准加法功能
忽略进位输出
模数加法：相当于增加一个模运算

## Slide 49: Visualizing (Mathematical) Integer Addition
Integer Addition
  4-bit integers u, v
  Compute true sum Add4(u , v)
  Values increase linearly with u and v
  Forms planar surface
Add4(u , v)
u
v

## Slide 50: Visualizing Unsigned Addition
Wraps Around
  If true sum ≥ 2w
  At most once
0
2w
2w+1
UAdd4(u , v)
u
v
True Sum
Modular Sum
Overflow
Overflow

## Slide 51: Mathematical Properties
Modular Addition Forms an Abelian Group
  Closed under addition
    0  UAddw(u , v)  2w –1
  Commutative
    UAddw(u , v) = UAddw(v , u)
  Associative
    UAddw(t, UAddw(u , v)) = UAddw(UAddw(t, u ), v)
  0 is additive identity
    UAddw(u , 0) = u
  Every element has additive inverse
    Let UCompw (u ) = 2w – u UAddw(u , UCompw (u )) = 0
Notes: 阿贝尔群（Abelian Group），又称交换群或加群，是这样一类群：
它由自身的集合 G 和二元运算 * 构成。它除了满足一般的群公理，即运算的结合律、G 有单位元、所有 G 的元素都有逆元之外，还满足交换律公理。因为阿贝尔群的群运算满足交换律和结合律，群元素乘积的值与乘法运算时的次序无关。
模数加法构成阿贝尔群（Modular Addition Forms an Abelian Group
  封闭性：0  UAddw(u , v)  2w –1
  交换性：UAddw(u , v) = UAddw(v , u)
  结合性：UAddw(t, UAddw(u , v)) = UAddw(UAddw(t, u ), v)
  单位元: 0
    UAddw(u , 0) = u
  每个元素都有逆元
    u的逆元 UCompw (u ) = 2w – u 则：UAddw(u , UCompw (u )) = 0

## Slide 52: Two’s Complement Addition
TAdd and UAdd have Identical Bit-Level Behavior
  Signed vs. unsigned addition in C:
  int s, t, u, v;
  s = (int) ((unsigned) u + (unsigned) v);
  t = u + v
  Will give s == t
• • •
• • •
u
v
+
• • •
u + v
• • •
True Sum: w+1 bits
Operands: w bits
Discard Carry: w bits
TAddw(u , v)

## Slide 53: TAdd Overflow
Functionality
  True sum requires w+1 bits
  Drop off MSB
  Treat remaining bits as 2’s comp. integer
–2w –1–1
–2w
0
2w –1
2w–1
True Sum
TAdd Result
1 000…0
1 011…1
0 000…0
0 100…0
0 111…1
100…0
000…0
011…1
PosOver
NegOver
Notes: 真实和需要w+1位
丢弃最高有效位（MSB）
将剩余的位视作补码（整数）

## Slide 54: Visualizing 2’s Complement Addition
Values
  4-bit two’s comp.
  Range from -8 to +7
Wraps Around
  If sum  2w–1
    Becomes negative
    At most once
  If sum < –2w–1
    Becomes positive
    At most once
TAdd4(u , v)
u
v
PosOver
NegOver

## Slide 55: Characterizing TAdd
Functionality
  True sum requires w+1 bits
  Drop off MSB
  Treat remaining bits as 2’s comp. integer
(NegOver)
(PosOver)
u
v
< 0
> 0
< 0
> 0
Negative Overflow
Positive Overflow
TAdd(u , v)
2w
2w
Notes: 其实判断补码是否超范围：u+v = r
uh!=vh 或者 uh==vh==rh 则正常
uh==vh!=rh 则溢出

## Slide 56: Mathematical Properties of TAdd
Isomorphic Group to unsigneds with UAdd
  TAddw(u , v) = U2T(UAddw(T2U(u ), T2U(v)))
    Since both have identical bit patterns
Two’s Complement Under TAdd Forms a Group
  Closed, Commutative, Associative, 0 is additive identity
  Every element has additive inverse
Notes: 与带Uadd加法的无符号数是同构群
TAddw(u , v) = U2T(UAddw(T2U(u ), T2U(v)))
因为两者具有相同的位模式
补码加法Tadd构成一个群
封闭性、 交换性、结合性、0是单位元
每个元素都有逆元

## Slide 57: Multiplication
Computing Exact Product of w-bit numbers x, y
  Either signed or unsigned
Ranges
  Unsigned: 0 ≤ x * y ≤ (2w – 1) 2 = 22w – 2w+1 + 1
    Up to 2w bits
  Two’s complement min: x * y ≥ (–2w–1)*(2w–1–1) = –22w–2 + 2w–1
    Up to 2w–1 bits
  Two’s complement max: x * y ≤ (–2w–1) 2 = 22w–2
    Up to 2w–2 bits, but only for (TMinw)2
Maintaining Exact Results
  Would need to keep expanding word size with each product computed
  Done in software by “arbitrary precision” arithmetic packages
Notes: 目标: 计算w位的两个数x和 y的乘积
有符号数或者无符号数
乘积的精确结果可能超过 w 位
1) 为获得精确结果可乘积的无符号数最多可达 2w 位
结果范围: 0 ≤ x * y ≤ (2w – 1)2 = 22w – 2w+1 + 1
2) 补码的最小值 (负数)最多需要2w-1 位
结果范围: x * y ≥ (–2w–1)*(2w–1–1) = –22w–2 + 2w–1
3) 补码最大值(正数)最多需要2w-2位——值为 (TMinw)2
结果范围: x * y ≤ (–2w–1)2 = 22w–2
最多需要2w位表示结果
扩展乘积的字长
在需要时用软件方法完成，例如： 算术程序包“arbitrary precision”

## Slide 58: Unsigned Multiplication in C
Standard Multiplication Function
  Ignores high order w bits
Implements Modular Arithmetic
  UMultw(u , v) = u · v mod 2w
• • •
• • •
u
v
*
• • •
u · v
• • •
True Product: 2*w bits
Operands: w bits
Discard w bits: w bits
UMultw(u , v)
• • •
Notes: 标准乘法功能
忽略高w 位
相当于对乘积执行了模运算

## Slide 59: Signed Multiplication in C
Standard Multiplication Function
  Ignores high order w bits
  Some of which are different for signed vs. unsigned multiplication
  Lower bits are the same
• • •
• • •
u
v
*
• • •
u · v
• • •
True Product: 2*w bits
Operands: w bits
Discard w bits: w bits
TMultw(u , v)
• • •
Notes: 标准乘法功能
忽略高w 位
有符号数乘、无符号数乘有不同之处
乘积的符号扩展
乘积的低位相同
先补最高位，连同取反加一

## Slide 60: Code Security Example #2
SUN XDR library
  Widely used library for transferring data between machines
void* copy_elements(void *ele_src[], int ele_cnt, size_t ele_size);
ele_src
malloc(ele_cnt * ele_size)

## Slide 61: XDR Code
void* copy_elements(void *ele_src[], int ele_cnt, size_t ele_size) {
/*
* Allocate buffer for ele_cnt objects, each of ele_size bytes
* and copy from locations designated by ele_src
*/
void *result = malloc(ele_cnt * ele_size);
if (result == NULL)
/* malloc failed */
return NULL;
void *next = result;
int i;
for (i = 0; i < ele_cnt; i++) {
/* Copy object i to destination */
memcpy(next, ele_src[i], ele_size);
/* Move pointer to next memory region */
next += ele_size;
}
return result;
}

## Slide 62: XDR Vulnerability
What if:
  ele_cnt = 220 + 1
  ele_size = 4096 = 212
  Allocation = ??
How can I make this function secure?
malloc(ele_cnt * ele_size)

## Slide 63: Power-of-2 Multiply with Shift
Operation
  u << k gives u * 2k
  Both signed and unsigned
Examples
  u << 3 == u * 8
  u << 5 - u << 3 == u * 24
  Most machines shift and add faster than multiply
    Compiler generates this code automatically
• • •
0
0
1
0
0
0
•••
u
2k
*
u · 2k
True Product: w+k bits
Operands: w bits
Discard k bits: w bits
UMultw(u , 2k)
•••
k
• • •
0
0
0
•••
TMultw(u , 2k)
0
0
0
•••
•••
Notes: Historically, the integer multiply instruction on many machines was fairly slow, requiring 10 or more clock cycles, whereas other integer operations—such as addition, subtraction, bit-level operations, and shifting—required only 1 clock cycle. Even on the Intel Core i7 Haswell we use as our reference machine, integer multiply requires 3 clock cycles. As a consequence, one important optimization used by compilers is to attempt to replace multiplications by constant factors with combinations of shift and addition operations.

## Slide 64: Unsigned Power-of-2 Divide with Shift
Quotient of Unsigned by Power of 2
  u >> k gives  u / 2k 
  Uses logical shift
0
0
1
0
0
0
•••
u
2k
/
u / 2k
Division:
Operands:
•••
k
•••
•••
•••
0
0
0
•••
•••
 u / 2k 
•••
Result:
.
Binary Point
0
0
0
0
•••
0
Notes: Integer division on most machines is even slower than integer multiplication— requiring 30 or more clock cycles. Dividing by a power of 2 can also be performed using shift operations, but we use a right shift rather than a left shift. The two different right shifts—logical and arithmetic—serve this purpose for unsigned and two’s-complement numbers, respectively.
floor, ceil and round

## Slide 65: Signed Power-of-2 Divide with Shift
0
0
Quotient of Signed by Power of 2
  u >> k gives  u / 2k 
  Uses arithmetic shift
  Rounds wrong direction when u < 0
0
0
1
0
0
0
•••
u
2k
/
u / 2k
Division:
Operands:
•••
k
•••
•••
•••
•••
•••
RoundDown(u / 2k)
•••
Result:
.
Binary Point
•••

## Slide 66: Correct Power-of-2 Divide
Quotient of Negative Number by Power of 2
  Want  x / 2k  (Round Toward 0)
  Compute as  (x+2k-1)/ 2k 
    In C: (x + (1<<k)-1) >> k
    Biases dividend toward 0
Case 1: No rounding
Divisor:
Dividend:
0
0
1
0
0
0
•••
u
2k
/
 u / 2k 
•••
k
1
•••
0
0
0
•••
1
•••
0
1
1
•••
.
Binary Point
1
0
0
0
1
1
1
•••
+2k –1
•••
1
1
1
•••
1
•••
1
1
1
•••
    Biasing has no effect
Notes: Proof: suppose x = qy + r, where 0 <= r < y
Giving (x + y – 1) / y = q + (r + y – 1)/y
Then ceil(x + y – 1) / y) = q + ceil(r + y – 1) / y).
If r = 0, then the latter term = 0;
Else if r > 0, then the latter term = 1.

## Slide 67: Correct Power-of-2 Divide (Cont.)
Divisor:
Dividend:
0
0
1
0
0
0
•••
x
2k
/
 x / 2k 
•••
k
1
•••
•••
1
•••
0
1
1
•••
.
Binary Point
1
0
0
0
1
1
1
•••
+2k –1
•••
1
•••
•••
    Biasing adds 1 to final result
•••
Incremented by 1
Incremented by 1
Case 2: Rounding

## Slide 68: Arithmetic: Basic Rules
Addition:
  Unsigned/signed: Normal addition followed by truncate, same operation on bit level
  Unsigned: addition mod 2w
    Mathematical addition + possible subtraction of 2w
  Signed: modified addition mod 2w (result in proper range)
    Mathematical addition + possible addition or subtraction of 2w
Multiplication:
  Unsigned/signed: Normal multiplication followed by truncate, same operation on bit level
  Unsigned: multiplication mod 2w
  Signed: modified multiplication mod 2w (result in proper range)
Notes: 加法:
  无/有符号数的加法: 正常加法后再截断,位级的运算相同
  无符号数:加后对2w求模
    数学加法 + 可能减去 2w
  有符号数: 修改的加后对 2w 求模，使结果在合适范围
    数学加法 + 可能减去或加上 2w
乘法:
  无/有符号数的乘法:正常乘法后加截断操作,位级运算相同
  无符号数:乘后对2w求模
  有符号数: 修改的乘后对 2w 求模，使结果在合适范围内

## Slide 69: Arithmetic: Basic Rules
Unsigned ints, 2’s complement ints are isomorphic rings: isomorphism = casting
Left shift
  Unsigned/signed: multiplication by 2k
  Always logical shift
Right shift
  Unsigned: logical shift, div (division + round to zero) by 2k
  Signed: arithmetic shift
    Positive numbers: div (division + round to zero) by 2k
    Negative numbers: div (division + round away from zero) by 2k Use biasing to fix
Notes: 无符号整数、补码整数是同构环(isomorphic rings)
  同构 = 类型转换 (isomorphism = casting)
左移
  无论有/无符号数，都可用逻辑左移实现乘以 2k
右移
  无符号数: 逻辑右移,除以 2k (除法 +向0舍入)
  有符号数: 算术右移
    正整数:除以 2k (除法 + 向0舍入)
    负整数:除以 2k (除法 + 远离0舍入)，使用偏置来修正

## Slide 70: Properties of Unsigned Arithmetic
Unsigned Multiplication with Addition Forms Commutative Ring
  Addition is commutative group
  Closed under multiplication
    0  UMultw(u , v)  2w –1
  Multiplication Commutative
    UMultw(u , v) = UMultw(v , u)
  Multiplication is Associative
    UMultw(t, UMultw(u , v)) = UMultw(UMultw(t, u ), v)
  1 is multiplicative identity
    UMultw(u , 1) = u
  Multiplication distributes over addtion
    UMultw(t, UAddw(u , v)) = UAddw(UMultw(t, u ), UMultw(t, v))

## Slide 71: Properties of Two’s Comp. Arithmetic
Isomorphic Algebras
  Unsigned multiplication and addition
    Truncating to w bits
  Two’s complement multiplication and addition
    Truncating to w bits
Both Form Rings
  Isomorphic to ring of integers mod 2w
Comparison to (Mathematical) Integer Arithmetic
  Both are rings
  Integers obey ordering properties, e.g.,
    u > 0  u + v > v
    u > 0, v > 0  u · v > 0
  These properties are not obeyed by two’s comp. arithmetic
    TMax + 1 == TMin
    15213 * 30426 == -10030 (16-bit words)

## Slide 72: Why Should I Use Unsigned?
Don’t Use Just Because Number Nonnegative
  Easy to make mistakes
    unsigned i;
    for (i = cnt-2; i >= 0; i--)
    a[i] += a[i+1];
  Can be very subtle
    #define DELTA sizeof(int)
    int i;
    for (i = CNT; i-DELTA >= 0; i-= DELTA)
    . . .
Do Use When Implementing Mathematical Packages
  For multiprecision arithmetic
Do Use When Using Bits to Represent Sets
  Logical right shift, no sign extension
Notes: sizeof操作符的结果类型是size_t,它在头文件中typedef为unsigned int类型
使用无符号类型循环变量的适当方法
    unsigned i;
    for (i = cnt-2; i < cnt; i--)
    a[i] += a[i+1];
参考Robert Seacord著《Secure Coding in C and C++》
  C 语言标准确保无符号数加法的行为与模运算类似
    0 – 1  UMax
好方法
    size_t i;
    for (i = cnt-2; i < cnt; i--)
    a[i] += a[i+1];
  size_t 定义为长度为计算机程序相同字长的无符号数
  即便cnt = Umax也能很好工作
  若cnt 是有符号数，且值小于0，会如何？
需要进行模运算的时候，就用无符号数
  多精度的算术运算
用二进制位表示集合时，就用无符号数
  逻辑右移、无符号扩展