## Slide 1: Unsigned & Signed Numeric Values
Equivalence
  Same encodings for nonnegative values
Uniqueness
  Every bit pattern represents unique integer value
  Each representable integer has unique bit encoding
 Can Invert Mappings
  U2B(x) = B2U-1(x)
    Bit pattern for unsigned integer
  T2B(x) = B2T-1(x)
    Bit pattern for two’s comp integer
X
B2T(X)
B2U(X)
0000
0
0001
1
0010
2
0011
3
0100
4
0101
5
0110
6
0111
7
–8
8
–7
9
–6
10
–5
11
–4
12
–3
13
–2
14
–1
15
1000
1001
1010
1011
1100
1101
1110
1111
0
1
2
3
4
5
6
7
Notes: 相同
  非负数值的编码相同
单值性
  每个位模式对应一个唯一的整数值
  每个可描述整数有一个唯一编码
 有逆映射
  U2B(x) = B2U-1(x)
    无符号整数的位模式
  T2B(x) = B2T-1(x)
    补码的位模式

## Slide 2: Sign Extension
Task:
  Given w-bit signed integer x
  Convert it to w+k-bit integer with same value
Rule:
  Make k copies of sign bit:
  X  = xw–1 ,…, xw–1 , xw–1 , xw–2 ,…, x0
k copies of MSB
• • •
X
X 
• • •
• • •
• • •
w
w
k

## Slide 3: Multiplication
1 0001
4 x 0100
0000
0000
0001
0000 0
xxxxxxxx
4 00000100
-7 1001
4 x 0100
0000
0000
111001
0000 0
xxxxxxxx
-28 11100100
1 0001
-4 x 1100
0000
0000
0001
11111 0
xxxxxxxx
-4 11111100
-7 1001
-4 x 1100
00000000
0000000
111001
00111 0 (符号位1，同上)
xxxxxxxx
28 100011100
符号位1，我们取反+1：0001->1110->1111，
高位补齐，低位添0
->（1）1111(000)

## Slide 4
Lei Wu
Zhejiang University

## Slide 5
Many images and resources used in this lecture are collected from the Internet, and they are used only for the educational purpose. The copyright belong to the original owners, respectively.
Part of slides credit to
  CSAPP @ CMU
  Prof. Yabo Dong @ ZJU
Disclaimer

## Slide 6: Representation of Numeric Data
Fixed-point number representation
Representation of integers
Floating-point number representation
Binary codes for decimal digits

## Slide 7: Reflect on Fractional Binary Numbers
2i
2i-1
4
2
1
1/2
1/4
1/8
2-j
bi | bi-1 | ••• | b2 | b1 | b0 | b-1 | b-2 | b-3 | ••• | b-j
Carnegie Mellon
• • •
Representation
  Bits to right of “binary point” represent fractional powers of 2
  Represents rational number:
• • •
Notes: 浮点表示很有用
对形如 V=x×2^𝑦 的有理数进行编码
非常大的数(|V|≫0 )或非常接近0的数(|V|≪1)
实数的近似值
无穷大/小怎么办？
从程序员角度看
无趣
晦涩难懂

## Slide 8: Limitation of Fractional Binary Numbers
Carnegie Mellon
Approximate representation
  Can only exactly represent numbers of the form x/2k
  Other rational numbers have repeating bit representations
  Value Representation
    1/3 0.0101010101[01]…2
    1/5 0.001100110011[0011]…2
    1/10 0.0001100110011[0011]…2
Implementation issues
  Limited bit width
  How to determine the binary point?
Notes: 局限性 1——近似表示
只能精确表示形如 x/2k的数值
其他有理数的二进制表示存在重复段
局限性 2
在计算机内的实现问题
长度有限的 w位
只能在w位内设置一个二进制小数点
限制了数的范围(非常小? 非常大?)
定点数
小数点隐含在w位编码的某一个固定位置上
例如MSB做符号位，隐含后面是小数点，表示小于1.0的纯小数
123.456怎么办？？？

## Slide 9: Floating-point Number Representation
IEEE floating point standard: Definition
Example and properties
Rounding, addition, multiplication
Floating point in C
Summary

## Slide 10: IEEE Floating Point
Carnegie Mellon
IEEE Standard 754
  Designed by William Kahan since 1976
  Established in 1985 as uniform standard for floating point arithmetic
    Before that, many idiosyncratic formats
  Supported by all major CPUs
Driven by numerical concerns
  Nice standards for rounding, overflow, underflow
  Hard to make fast in hardware
    Numerical analysts predominated over hardware designers in defining standard
Notes: IEEE 标准 754
William Kahan 从1976年开始为Intel 设计(1989获图灵奖)
1985年成为浮点运算的统一标准，快速, 易于实现、精度损失小
优雅、易理解
所有主流的CPU都支持
之前有很多不同格式、不太关注精确性

## Slide 11: Floating Point Representation
Carnegie Mellon
Numerical Form: (–1)s M 2E
  Sign bit s determines whether number is negative or positive
  Significand M normally a fractional value in range [1.0,2.0).
  Exponent E weights value by power of two
Encoding
  MSB s is sign bit s
  exp field encodes E (but is not equal to E)
  frac field encodes M (but is not equal to M)
s | exp | frac
Notes: 符号(sign)s， 决定数的符号，是正数(s=0)或负数(s=1)
尾数(Significand) M，二进制小数，数值范围: [1.0,2.0)
阶码(Exponent) E ，用2E将数值加权
浮点数编码
最高有效位(MSB)s，作为符号位s
exp 字段 编码E (和E不一定相等)
frac 字段编码尾数 M (和M不一定相等)

## Slide 12: Precisions
Carnegie Mellon
Single precision: 32 bits
Double precision: 64 bits
Extended precision: 80 bits (Intel only)
s | exp | frac
1 | 8-bits | 23-bits
s | exp | frac
1 | 11-bits | 52-bits
s | exp | frac
1 | 15-bits | 63 or 64-bits

## Slide 13: Exponent (Frameshift Code)
E |  |  | EXP-----IEEE754 | IEEE754 | 
True Value | Complement | Shift+128 | Shift+127 | Machine Number | 
127 | 01111111 | 11111111 | 11111110 | 254 | 
126 | 01111110 | 11111110 | 11111101 | 253 | 
……… | ……… | ……… |  | ……… | 
2 | 00000010 | 10000010 | 10000001 | 129 | 
1 | 00000001 | 10000001 | 10000000 | 128 | 
0 | 00000000 | 10000000 | ‘01111111 | 127 | 
-1 | 11111111 | ‘01111111 | ’01111110 | 126 | 
-2 | 11111110 | ’01111110 | ‘01111101 | 125 | 
……… | ……… | ……… | ……… | ……… | 
-126 | 10000010 | ‘00000010 | ’00000001 | 1 | 
-127 | 10000001 | ’00000001 | ‘00000000 | 0 | Invalid
-128 | 10000000 | ‘00000000 | 11111111 | -1 | Invalid
Notes: 采用指数的实际值加上固定的偏移值的办法表示浮点数的指数，好处是可以用长度为e个比特的无符号整数来表示所有的指数取值，这使得两个浮点数的指数大小的比较更为容易（不用考虑符号位），实际上可以按照字典序比较两个浮点数的大小。
This is the most common case. It occurs when the bit pattern of exp is neither all zeros (numeric value 0) nor all ones (numeric value 255 for single precision, 2047 for double). In this case, the exponent field is interpreted as representing a signed integer in biased form.
When the exponent field is all zeros, the represented number is in denormalized form. In this case, the exponent value is E = 1 − Bias, and the significand value is M = f , that is, the value of the fraction field without an implied leading 1.
Having the exponent value be 1 − Bias rather than simply −Bias might seem counterintuitive. We will see shortly that it provides for smooth transition from denormalized to normalized values.

## Slide 14: Normalized Values
Carnegie Mellon
Condition: exp ≠ 000…0 and exp ≠ 111…1
Exponent coded as biased value: E = Exp – Bias
  Exp: unsigned value exp
  Bias = 2k-1 - 1, where k is number of exponent bits
    Single precision: 127 (Exp: 1…254, E: -126…127)
    Double precision: 1023 (Exp: 1…2046, E: -1022…1023)
Significand coded with implied leading 1:
M = 1.xxx…x2
  xxx…x: bits of frac
  Minimum when 000…0 (M = 1.0)
  Maximum when 111…1 (M = 2.0 – ε)
  Get extra leading bit for “free”
Notes: 规格化数
条件: exp ≠ 000…0 且 exp ≠ 111…1
阶码(Exponent) 采用偏置值编码: E = Exp – Bias
Exp: exp 字段的无符号数值
偏置Bias = 2k-1 - 1, k 为阶码的位数
单精度: 127 (Exp: 1…254, E: -126…127)
双精度: 1023 (Exp: 1…2046, E: -1022…1023)
尾数(Significand) 编码隐含先导数值1: M = 1.xxx…x2
xxx…x: 是 frac字段的数码
frac=000…0 (M = 1.0)时，为最小值
frac=111…1 (M = 2.0 – ε)时，为最大值
额外增加了一位的精度（隐含值1）

## Slide 15: Normalized Encoding Example
Value: Float F = 15213.0;
  1521310 = 111011011011012
  = 1.11011011011012 x 213
Significand
  M = 1.11011011011012
  frac = 110110110110100000000002
Exponent
  E = 13
  Bias = 127
  Exp = 140 = 100011002
Result: 0 10001100 11011011011010000000000
s
exp
frac

## Slide 16: Denormalized Values
Carnegie Mellon
Condition: exp = 000…0
  Exponent value: E = –Bias + 1 (instead of E = 0 – Bias)
  Significand coded with implied leading 0: M = 0.xxx…x2
    xxx…x: bits of frac
Cases
  exp = 000…0, frac = 000…0
    Represents zero value
    Note distinct values: +0 and –0 (why?)
  exp = 000…0, frac ≠ 000…0
    Numbers very close to 0.0
    Lose precision as get smaller
    Equispaced: abrupt underflow vs. gradual underflow
Notes: 条件: exp = 000…0
阶码(Exponent) 值: E = 1 – Bias =-126/-1022(instead of E = 0 – Bias)
尾数(Significand)编码隐含先导数值0: M = 0.xxx…x2
xxx…x:是 frac字段的数码
情况1： exp = 000…0, frac = 000…0
表示值0
注意有不同的数值 +0 和 –0 (why?)
情况2：exp = 000…0, frac ≠ 000…0
最接近0.0的那些数
间隔均匀：突然式下溢出(abrupt underflow) 和 渐进式下溢出(gradual underflow)
IEEE754-1985标准采用非规约浮点数，用来解决填补绝对值意义下最小规约数与零的距离。
非规约浮点数源于70年代末IEEE浮点数标准化专业技术委员会酝酿浮点数二进制标准时，Intel公司对渐进式下溢出（gradual underflow）的力荐。而当时十分流行的DECVAX机的浮点数表示采用了突然式下溢出（abrupt underflow）。
如果没有渐进式下溢出，那么0与绝对值最小的浮点数之间的距离（gap）将大于相邻的浮点数之间的距离。例如单精度浮点数的绝对值最小的规约浮点数是2-126,绝对值次小的规约浮点数为（1 + 2-23） * 2-126,这两个数之间的距离为（1 + 2-23） * 2-126 - 2-126 = 2-149。而2-126与0之间的距离为2-126，如果不采用渐进式下溢出，那么绝对值最小的规约浮点数与0的距离是相邻的小浮点数之间距离的223倍！可以说是非常突然的下溢出到0。
采用了渐进式下溢出后将不会出现这种情况。例如对于单精度浮点数，指数部分实际最小值是（-126），对应的尾数部分从000……000,000……001，000……010，000……011 一直到111……101，111……110，111……111，每两个相邻两小浮点数之间的距离（gap）都是2-126 * 2-23 = 2-149；而0与最近的浮点数（即最小的非规约数）之间的距离也是2-149。

## Slide 17: Special Values
Carnegie Mellon
Condition: exp = 111…1
Case: exp = 111…1, frac = 000…0
  Represents value  (infinity)
  Operation that overflows
  Both positive and negative
  E.g., 1.0/0.0 = −1.0/−0.0 = +, 1.0/−0.0 = −
Case: exp = 111…1, frac ≠ 000…0
  Not-a-Number (NaN)
  Represents case when no numeric value can be determined
  E.g., sqrt(–1),  − ,   0
Notes: 条件: exp = 111…1
情况1: exp = 111…1, frac = 000…0
表示 无穷(infinity) 
溢出的运算
正无穷、负无穷
情况2: exp = 111…1, frac ≠ 000…0
表示：不是一个数Not-a-Number (NaN)
表示没有数值结果（实数或无穷）

## Slide 18: Normalized vs. Denormalized Values
Carnegie Mellon
2-126
2-125
2-124
2-123
[1.0…0x2-126~ 1.1…1x2-126)
0.0…0x2-126~ 0.1…1x2-126
2-126
2-125
2-124
2-123
0
0
GAP
Normalized values
Denormalized values
(-1)s×0.xx…x ×2-126
Notes: 注意浮点数的密度与分布
As we know, in IEEE standard, normalized numbers are those with the form: +/- 1.aa…a x 2bb…b, where aa…a can be anything(from 00…0 to 11…1), bb…b can be from 00…01 ( the value is 1-127=-126) to 11…10 (the value is 254-127=127). Considering positive number, the smallest number is 1.00…0 x 2-126 . Between 0 and the smallest number there is a big gap. IEEE use the combination of exponent=00…0 and significand=nonzero to fill in this gap. These number are called denormalized numbers. We briefly call them denorms. In denorm form, the exponent is always 00…0, and no implicit leading 1, the significand is nonzero bit pattern. It means denormalized numbers have form of +/- 0.aa…a x 2-126 , here aa…a can be 0.00…01, 0.000…10, ……., 0.11…1.

## Slide 19: Special Values
Carnegie Mellon
Condition: exp = 111…1
Case: exp = 111…1, frac = 000…0
  Represents value  (infinity)
  Operation that overflows
  Both positive and negative
  E.g., 1.0/0.0 = −1.0/−0.0 = +, 1.0/−0.0 = −
Case: exp = 111…1, frac ≠ 000…0
  Not-a-Number (NaN)
  Represents case when no numeric value can be determined
  E.g., sqrt(–1),  − ,   0
Notes: 条件: exp = 111…1
情况1: exp = 111…1, frac = 000…0
表示 无穷(infinity) 
溢出的运算
正无穷、负无穷
情况2: exp = 111…1, frac ≠ 000…0
表示：不是一个数Not-a-Number (NaN)
表示没有数值结果（实数或无穷）

## Slide 20: Visualization: Floating Point Encodings
Carnegie Mellon
+
−
0
+Denorm
+Normalized
−Denorm
−Normalized
+0
NaN
NaN

## Slide 21: Tiny Floating Point Example
Carnegie Mellon
8-bit Floating Point Representation
  the sign bit is in the most significant bit
  the next four bits are the exponent, with a bias of 7
  the last three bits are the frac
Same general form as IEEE Format
  normalized, denormalized
  representation of 0, NaN, infinity
s | exp | frac
1 | 4-bits | 3-bits

## Slide 22: Dynamic Range (Positive Only)
Carnegie Mellon
s exp frac E Value
0 0000 000 -6 0
0 0000 001 -6 1/8*1/64 = 1/512
0 0000 010 -6 2/8*1/64 = 2/512
…
0 0000 110 -6 6/8*1/64 = 6/512
0 0000 111 -6 7/8*1/64 = 7/512
0 0001 000 -6 8/8*1/64 = 8/512
0 0001 001 -6 9/8*1/64 = 9/512
…
0 0110 110 -1 14/8*1/2 = 14/16
0 0110 111 -1 15/8*1/2 = 15/16
0 0111 000 0 8/8*1 = 1
0 0111 001 0 9/8*1 = 9/8
0 0111 010 0 10/8*1 = 10/8
…
0 1110 110 7 14/8*128 = 224
0 1110 111 7 15/8*128 = 240
0 1111 000 n/a inf
closest to zero
largest denorm
smallest norm
closest to 1 below
closest to 1 above
largest norm
Denormalized
numbers
Normalized
numbers

## Slide 23: Distribution of Values
Carnegie Mellon
6-bit IEEE-like format
  e = 3 exponent bits
  f = 2 fraction bits
  Bias is 23-1-1 = 3
Notice how the distribution gets denser toward zero.
8 values
s | exp | frac
1 | 3-bits | 2-bits

## Slide 24: Distribution of Values (close-up view)
Carnegie Mellon
6-bit IEEE-like format
  e = 3 exponent bits
  f = 2 fraction bits
  Bias is 3
s | exp | frac
1 | 3-bits | 2-bits

## Slide 25: Interesting Nonnegative Numbers
Carnegie Mellon
Description exp frac Numeric Value
Zero 00…00 00…00 0.0
Smallest Pos. Denorm. 00…00 00…01 2– {23,52} x 2– {126,1022}
  Single ≈ 1.4 x 10–45
  Double ≈ 4.9 x 10–324
Largest Denormalized 00…00 11…11 (1.0 – ε) x 2– {126,1022}
  Single ≈ 1.18 x 10–38
  Double ≈ 2.2 x 10–308
Smallest Pos. Normalized 00…01 00…00 1.0 x 2– {126,1022}
  Just larger than largest denormalized
One 01…11 00…00 1.0
Largest Normalized 11…10 11…11 (2.0 – ε) x 2{127,1023}
  Single ≈ 3.4 x 1038
  Double ≈ 1.8 x 10308
{single,double}

## Slide 26: Special Properties of Encoding
Carnegie Mellon
FP Zero Same as Integer Zero
  All bits = 0
Can (Almost) Use Unsigned Integer Comparison
  Must first compare sign bits
  Must consider −0 = 0
  NaNs problematic
    Will be greater than any other values
    What should comparison yield?
  Otherwise OK
    Denorm vs. normalized
    Normalized vs. infinity
Notes: 浮点0与整数0编码相同：所有bit均为0
几乎可以用与无符号整数相同的方式进行浮点数的比较
先比较符号位
必须考虑 −0 = 0
NaN的不确定性
将比其他任何值都大
比较将产生什么结果？
其他方面均OK
规格化值 vs. 非规格化值
规格化值 vs. 无穷

## Slide 27: Floating Point Operations: Basic Idea
Carnegie Mellon
x +f y = Round(x + y)
x f y = Round(x  y)
Basic idea
  First compute exact result
  Make it fit into desired precision
    Possibly overflow if exponent too large
    Possibly round to fit into frac
Notes: 基本思想
首先，计算精确结果
然后，变换到指定格式
可能溢出：阶码(Exponent) 太大
小数部分可能需要舍入

## Slide 28: Rounding
Carnegie Mellon
Rounding Modes (illustrate with $ rounding)
$1.40 $1.60 $1.50 $2.50 –$1.50
  Towards zero $1 $1 $1 $2 –$1
  Round down (−) $1 $1 $1 $2 –$2
  Round up (+) $2 $2 $2 $3 –$1
  Nearest Even (default) $1 $2 $2 $2 –$2
What are the advantages of the modes?
Notes: The IEEE floating-point format defines four different rounding modes.
The default method finds a closest match, while the other three can be used for computing upper and lower bounds.
舍入到最接近且可以表示的值，当存在两个数一样接近时，取偶数值。(如2.4舍入为2，2.6舍入为3；2.5舍入为2，1.5舍入为2。)
Q：为什么会当存在两个数一样接近时，取偶数值呢？
A：由于其他舍入方式均令结果单方向偏移，导致在运算时出现较大的统计偏差。而采用这种偏移则50%的机会偏移两端方向，从而减少偏差。
It attempts to find a closest match. Thus, it rounds $1.40 to $1 and $1.60 to $2, since these are the closest whole dollar values. The only design decision is to determine the effect of rounding values that are halfway between two possible results.
Round-to-even mode adopts the convention that it rounds the number either upward or downward such that the least significant digit of the result is even. Thus, it rounds both $1.50 and $2.50 to $2.
The other three modes produce guaranteed bounds on the actual value. These can be useful in some numerical applications.

## Slide 29: Closer Look at Round-To-Even
Carnegie Mellon
Default Rounding Mode
  Hard to get any other kind without dropping into assembly
  All others are statistically biased
    Sum of set of positive numbers will consistently be over- or under- estimated
Applying to Other Decimal Places / Bit Positions
  When exactly halfway between two possible values
    Round so that least significant digit is even
  E.g., round to nearest hundredth
    7.8949999 7.89 (Less than half way)
    7.8950001 7.90 (Greater than half way)
    7.8950000 7.90 (Half way—round up)
    7.8850000 7.88 (Half way—round down)
Notes: 默认的舍入模式
很难找到更好的方法
其他方法都有统计偏差
对正整数集合求和时，和将始终被低估或高估（负偏差、正偏差）
向偶数舍入
当恰好在两个可能的数值正中间时（中间值）： 舍入后，最低有效位的数码为偶数
其他时候：向最近的数值舍入
比中间值小向下舍入，比中间值大向上舍入
以10进制数向最近的百分位舍入为例：
7.8949999 7.89 (比中间值小：向下舍入)
7.8950001 7.90 (比中间值大：向上舍入)
7.8950000 7.90 (中间值—向上舍入)
7.8850000 7.88 (中间值—向下舍入)

## Slide 30: Rounding Binary Numbers
Carnegie Mellon
Binary Fractional Numbers
  “Even” when least significant bit is 0
  “Half way” when bits to right of rounding position = 100…2
Examples
  Round to nearest 1/4 (2 bits right of binary point)
  Value Binary Rounded Action Rounded Value
  2 3/32 10.000112 10.002 (<1/2—down) 2
  2 3/16 10.001102 10.012 (>1/2—up) 2 1/4
  2 7/8 10.111002 11.002 ( 1/2—up) 3
  2 5/8 10.101002 10.102 ( 1/2—down) 2 1/2
Notes: 二进制小数的舍入
“偶数”：最低有效位值为0
“中间值”：舍入位置右侧的位都是0，即形如: xxx 100…2
例子
舍入到最近的1/4 (小数点右边第2位)

## Slide 31: Floating Point Addition
Carnegie Mellon
(–1)s1 M1 2E1 + (-1)s2 M2 2E2
  Assume E1 > E2
Exact Result: (–1)s M 2E
  Sign s, significand M:
    Result of signed align & add
  Exponent E: E1
Fixing
  If M ≥ 2, shift M right, increment E
  if M < 1, shift M left k positions, decrement E by k
  Overflow if E out of range
  Round M to fit frac precision
(–1)s1 M1
(–1)s2 M2
E1–E2
+
(–1)s M
Notes: (–1)s1 M1 2E1 + (-1)s2 M2 2E2
  假设 E1 > E2
准确结果: (–1)s M 2E
  符号 s, 尾数M:
    有符号数对齐、相加的结果
  阶码(Exponent) E: E1
修正
  M ≥ 2：将M右移(1位)，E加1
  M < 1：将M左移k 位, E 减 k
  E超范围：溢出
  将M舍入，以符合小数部分的精度要求

## Slide 32: Mathematical Properties of FP Add
Carnegie Mellon
Compare to those of Abelian Group
  Closed under addition?
    But may generate infinity or NaN
  Commutative?
  Associative?
    Overflow and inexactness of rounding
  0 is additive identity?
  Every element has additive inverse
    Except for infinities & NaNs
  Monotonicity
    a ≥ b ⇒ a+c ≥ b+c?
    Except for infinities & NaNs
Yes
Yes
Yes
No
Almost
Almost
Notes: 与阿贝尔群比较
  加法运算下:
  是否封闭
    But may generate infinity or NaN
  交换性(Commutative)?
  分配性(Associative)?
    溢出和舍入的不确定性
    (3.14+1e10)-1e10 = 0, 3.14+(1e10-1e10) = 3.14
  0 是加法的单位元?
  每个元素都有逆元?
    除了无穷和NaN
单调性(Monotonicity)
  a ≥ b ⇒ a+c ≥ b+c?
    除了无穷和NaN

## Slide 33: Floating Point Multiplication
Carnegie Mellon
(–1)s1 M1 2E1 x (–1)s2 M2 2E2
Exact Result: (–1)s M 2E
  Sign s: s1 ^ s2
  Significand M: M1 x M2
  Exponent E: E1 + E2
Fixing
  If M ≥ 2, shift M right, increment E
  If E out of range, overflow
  Round M to fit frac precision
Implementation
  Biggest chore is multiplying significands
Notes: 精确结果: (–1)s M 2E
符号(Sign) s: s1 ^ s2
尾数(Significand) M: M1 x M2
阶码(Exponent) E: E1 + E2
修正
如M ≥ 2, 将M右移(1位), E加1
如 E 超出范围，则溢出
将M舍入，以符合小数部分的精度要求
实现
主要问题：实现尾数(Significand)的乘

## Slide 34: Mathematical Properties of FP Mult
Carnegie Mellon
Compare to Commutative Ring
  Closed under multiplication?
    But may generate infinity or NaN
  Multiplication Commutative?
  Multiplication is Associative?
    Possibility of overflow, inexactness of rounding
  1 is multiplicative identity?
  Multiplication distributes over addition?
    Possibility of overflow, inexactness of rounding
  Monotonicity
    a ≥ b & c ≥ 0 ⇒ a * c ≥ b *c?
    Except for infinities & NaNs
Yes
Yes
No
Yes
No
Almost
Notes: 与交换环相比
  乘法下封闭性？
    但可能产生无穷或NaN
  乘法的交换性？
  乘法的结合性？
    可能溢出、舍入不精确
    例: (1e20*1e20)*1e-20= inf, 1e20*(1e20*1e-20)= 1e20
  1 是乘法的单位元？
  乘法对加法的分配性？
    可能溢出、舍入不精确
    1e20*(1e20-1e20)= 0.0, 1e20*1e20 – 1e20*1e20 = NaN
单调性
  a ≥ b & c ≥ 0 ⇒ a * c ≥ b *c?
    除了无穷和 NaN

## Slide 35: Floating Point in C
Carnegie Mellon
C Guarantees Two Levels
  float single precision
  double double precision
Conversions/Casting
  Casting between int, float, and double changes bit representation
  double/float → int
    Truncates fractional part
    Like rounding toward zero
    Not defined when out of range or NaN: Generally sets to TMin
  int → double
    Exact conversion, as long as int has ≤ 53 bit word size
  int → float
    Will round according to rounding mode
Notes: 两种精度
  float 单精度
  double 双精度
类型转换
  int, float, double 间转换，将改变位模式
  double/float → int
    截掉小数部分
    类似向0舍入
    当数值超范围或NaN时无定义：通常设置为 TMin
  int → double
    精确转换,只要int的位宽 ≤ 53 bit，即可精确转换
  int → float
    将根据舍入模式进行舍入

## Slide 36: Floating Point Puzzles
Carnegie Mellon
For each of the following C expressions, either:
  Argue that it is true for all argument values
  Explain why not true
x == (int)(float) x
x == (int)(double) x
f == (float)(double) f
d == (float) d
f == -(-f);
2/3 == 2/3.0
d < 0.0 ⇒ ((d*2) < 0.0)
d > f ⇒ -f > -d
d * d >= 0.0
(d+f)-d == f
int x = …;
float f = …;
double d = …;
Assume neither
d nor f is NaN
Notes: x == (int)(float) x No: 24 位尾数
x == (int)(double) x Yes: 53位尾数
f == (float)(double) f Yes: 增加精度
d == (float) d No: 损失精度
f == -(-f); Yes: 仅仅改变符号位
2/3 == 2/3.0 No: 2/3 == 0
d < 0.0 ((d*2) < 0.0) Yes!
d > f  -f < -d Yes
d *d >= 0.0 Yes!
(d+f)-d == f No: 不具备结合性

## Slide 37: Summary
Carnegie Mellon
IEEE Floating Point has clear mathematical properties
Represents numbers of form M x 2E
One can reason about operations independent of implementation
  As if computed with perfect precision and then rounded
Not the same as real arithmetic
  Violates associativity/distributivity
  Makes life difficult for compilers & serious numerical applications programmers
    Some famous disasters caused by numerical errors
Notes: IEEE 浮点数 具有清晰的数学性质
表示形如 M x 2E 的数字
对运算进行推理，而不用考虑其实现
  就像有完美的精度，然后在进行舍入
和实数运算不同
  结合性、分配性有冲突
  日子变得难：编译器、认真的数值应用程序员
1991年2月25日
美国爱国者导弹拦截伊拉克飞毛腿导弹失败
后果：飞毛腿导弹炸死28名士兵
爱国者导弹的内置时钟计数器N每0.1秒记一次数。
时间计算
T = N×0.1
程序用24位数来近似表示0.1：
x=0.0001 1001 1001 1001 1001 100
0.1-x = 0.00000000000000000000000[1100][1100]…2
0.1-x = 2-20 ×0.1 = 9.54×10-8
程序运行100 后，累计的误差： 100×3600× 10×9.54×10-8 =0.34344秒
软件升级不完全，第一次读取了精确时间，而另一次读取了有误差的时间，结果悲剧….
飞毛腿速度：2000 m/s
飞毛腿位置的估计误差：686 m
主角：阿丽亚娜5(Ariane5)型火箭的首次发射
时间：1996.6.4
剧情：发射后仅37秒，偏离路径，解体爆炸
代价：5亿美元
原因：溢出
溢出——将64位浮点数转换成16位有符号整型数时，发生溢出。这个溢出的整型数，用于描述火箭的水平速度
Ariane4的水平速度绝对不会超过16位数的范围，因此用了16位整数
Ariane5简单复用了这部分代码
问题： Ariane 5 的水平速度是Ariane 4的5倍！！！

## Slide 38: Disasters Attributable to Bad Numerics
Carnegie Mellon
The Patriot Missile Failure
  On February 25, 1991, during the Gulf War, an American Patriot Missile battery in Dharan, Saudi Arabia, failed to track and intercept an incoming Iraqi Scud missile. The Scud struck an American Army barracks, killing 28 soldiers and injuring around 100 other people.
  It turns out that the cause was an inaccurate calculation of the time since boot due to computer arithmetic errors.
The Explosion of the Ariane 5
  On June 4, 1996, an unmanned Ariane 5 rocket launched by the European Space Agency exploded just forty seconds after its lift-off from Kourou, French Guiana. Ariane explosion. The rocket was on its first voyage, after a decade of development costing $7 billion. The destroyed rocket and its cargo were valued at $500 million.
  It turned out that the cause of the failure was a software error in the inertial reference system.
https://www-users.cse.umn.edu/~arnold/disasters/disasters.html
Notes: 1991年2月25日美国爱国者导弹拦截伊拉克飞毛腿导弹失败
后果：飞毛腿导弹炸死28名士兵
爱国者导弹的内置时钟计数器N每0.1秒记一次数。
时间计算
T = N×0.1
程序用24位数来近似表示0.1：
x=0.0001 1001 1001 1001 1001 100
0.1-x = 0.00000000000000000000000[1100][1100]…2
0.1-x = 2-20 ×0.1 = 9.54×10-8
程序运行100 hours 后，累计的误差： 100×3600× 10×9.54×10-8 =0.34344秒
软件升级不完全，第一次读取了精确时间，而另一次读取了有误差的时间，结果悲剧….
飞毛腿速度：1,676 m/s
飞毛腿位置的估计误差：686 m
主角：阿丽亚娜5(Ariane5)型火箭的首次发射
时间：1996.6.4
剧情：发射后仅37秒，偏离路径，解体爆炸
代价：5亿美元
原因：溢出
溢出——将64位浮点数转换成16位有符号整型数时，发生溢出。这个溢出的整型数，用于描述火箭的水平速度
Ariane4的水平速度绝对不会超过16位数的范围，因此用了16位整数
Ariane5简单复用了这部分代码
问题： Ariane 5 的水平速度是Ariane 4的5倍！！！

## Slide 39: Binary Codes for Decimal Digits
The computer needs to process decimal data, so it must be represented by binary numbers or Binary Coded Decimal (BCD) codes.
Weighted BCD Code: The weighted BCD code means that the four binary digits of the decimal digits have a certain right. The common used one is 8421 code.
No weight BCD Code: Commonly used coding schemes are Gray code and Excess3 code.
Notes: The BCD code is the 8,4,2,1 code.
8, 4, 2, and 1 are weights
BCD is a weighted code
This code is the simplest, most intuitive binary code for decimal digits and uses the same powers of 2 as a binary number, but only encodes the first ten values from 0 to 9.
Example: 1001 (9) = 1000 (8) + 0001 (1)
How many “invalid” code words are there?
What are the “invalid” code words?
Answer 1: 6
Answer 2: 1010, 1011, 1100, 1101, 1110, 1111

## Slide 40: DECIMAL CODES
Decimal
8,4,2,1
Excess3
8,4,
-
2,
-
1
Gray
0
0000
0011
0000
0000
1
0001
0100
0111
0100
2
0010
0101
0110
0101
3
0011
0110
0101
0111
4
0100
0111
0100
0110
5
0101
1000
1011
0010
6
0110
1001
1010
0011
7
0111
1010
1001
0001
8
1000
1011
1000
1001
9
1001
1
100
1111
1000
There are over 8,000 ways that you can chose 10 elements from the 16 binary numbers of 4 bits. A few are useful:
Notes: 格雷码特点是任意两个相邻的编码只有一位二进位不同，格雷码也有多种编码形式。
BCD码也有自己的运算方法，这里略过。

## Slide 41: Overview
Introduction to computer systems
Binary number representation
Arithmetic operations
Representation of numeric data
Representation of non-numeric data
Data width and storage

## Slide 42: Non-numeric Data
Primitive types
Numeric
Non-numeric
Integer number
(fixed-point)
Real number
(floating-point)
Unsigned
Signed
Bits
Character/
String
Low-level programmer’s/
hardware system designer’s perspective
Notes: 机器语言只有最基本的数据类型：
1）数值型数据：表示数量的多少，可比较大小。具体而言，整数（无符号，有符号）用定点数表示，以及实数用浮点数表示。
2）非数值型数据：字符和逻辑值。

## Slide 43: Representation of logical values
Under normal circumstances, each word or other addressable unit can be regarded as a whole data unit.
However, sometimes it is necessary to treat an n-bit data as consisting of n 1-bit data, each is 0 or 1.
Therefore, n-bit binary numbers can represent n logical values.
Notes: 逻辑数据和数值型数据都是0/1序列，形式上相同，需通过指令的操作码类型识别，比如逻辑运算指令处理逻辑数据，算术运算指令处理数值型数据。

## Slide 44: ALPHANUMERIC CODES - ASCII Character Codes
American Standard Code for Information Interchange
Represent information sent as character-based data
Use 7-bits to represent:
  94 Graphic printing characters.
  34 Non-printing characters
    Some non-printing characters are used for text format (e.g. BS = Backspace, CR = carriage return)
    Other non-printing characters are used for record marking and flow control (e.g. STX and ETX start and end text areas)
Notes: 计算机内部处理西文字符包括拉丁字母、数字、标点符号和一些特殊符号，所有字符集合构成字符集。
字符集每个字符都有一个代码，构成了字符集代码表，简称码表。主要用于外部设备和计算机之间交换信息。
最广泛使用的ASCII码，即美国标准信息交换码。
由7个bit表示，0-3低位，4-6高位。

## Slide 45: ASCII Properties
Digits 0 to 9 span Hexadecimal values 3016 to 3916
Upper case A-Z span 4116 to 5A16
Lower case a-z span 6116
  Lower to upper case translation (and vice versa) occurs by flipping bit 6
Delete (DEL) is all bits set
  A carryover from when punched paper tape was used to store messages
  Punching all holes in a row erased a mistake

## Slide 46: 7 BIT ASCII CODE TABLE
b6b5b4 b3b2b1b0 | 000 | 001 | 010 | 011 | 100 | 101 | 110 | 111
0000 | NUL | DLE | SP | 0 | @ | P | ， | p
0001 | SOM | DC | ! | 1 | A | Q | a | q
0010 | STX | DC | “ | 2 | B | R | b | r
0011 | ETX | DC | # | 3 | C | S | c | s
0100 | EOT | DC | $ | 4 | D | T | d | t
0101 | ENQ | NAA | % | 5 | E | U | e | u
0110 | ACA | SYN | & | 6 | F | V | f | v
0111 | BEL | ETB | ， | 7 | G | W | g | w
1000 | BS | CAN | ( | 8 | H | X | h | x
1001 | HT | EM | ) | 9 | I | Y | i | y
1010 | LF | SUB | * | : | J | Z | j | z
1011 | VT | ESC | + | ; | A | [ | k | 
1100 | FF | FS | ， | < | L | \ | l | ¦
1101 | CR | GS | － | = | M | ] | m | 
1110 | SO | RS | ． | > | N |  | n | ~
1111 | SI | US | / | ? | O | ← | o | DEL

## Slide 47: UNICODE
UNICODE extends ASCII to 65,536 universal characters codes
  For encoding characters in world languages
  Available in many modern applications
  2 byte (16-bit) code words
  See Reading Supplement – Unicode on the Companion Website http://www.prenhall.com/mano
Notes: 国际标准化组织制定Unicode编码。随着Unicode编码规范的建立，其实现方式有UTF-8，UTF-16，UTF-32。由于UTF-8采用变长的编码方式实现，其节省空间，兼容ASCII标准的优点， 在互联网上使用最广的一种Unicode的实现方式。

## Slide 48: Representation of Chinese Characters
The Chinese character system includes the following Chinese character codes: input code, internal code, font code.
Input Code: Chinese characters are encoded using the corresponding keys.
Internal Code: The internal code of Chinese characters consists of several rows and several columns. The row number is called the area code, and the column number is called the tag number.
Font Code
Notes: 汉字输入码包括：数字码（区位码）、拼音码、字形码
内码：
用于汉字信息的存储、转换、检索等操作的计算机内代码，一般用两字节表示。
国标码：10进制区位码转换为16进制，再加上2020H；
机内码：国标码+8080H（与ASCII区别），或者区位码转为16进制+A0A0H
输入码 -> 机内码 -> 字形码（显示）

## Slide 49: Overview
Introduction to computer systems
Binary number representation
Arithmetic operations
Representation of numeric data
Representation of non-numeric data
Data width and storage

## Slide 50: Data Width and Unit
Bit
  The smallest unit that makes up a binary number
Machine has “word size”
  Nominal size of integer-valued data
    Including addresses
  Most current machines use 32 bits (4 bytes) words
    Limits addresses to 4GB
    Becoming too small for memory-intensive applications
  High-end systems use 64 bits (8 bytes) words
    Potential address space ≈ 1.8 X 1019 bytes
    x86-64 machines support 48-bit addresses: 256 Terabytes
  Machines support multiple data formats
    Fractions or multiples of word size
    Always integral number of bytes
Notes: 机器字长
CPU中ALU的数据位数=CPU中通用寄存器的位数
通常计算机是XX位的，是指这台计算机CPU字的长度
字是用来表示处理信息的单位，ISA设计者必须考虑机器提供哪些数据类型，有哪几种宽度，这时就要给出一个基本的字的宽度。

## Slide 51: Data Representations
C Data Type | Typical 32-bit | Intel IA32 | x86-64
char | 1 | 1 | 1
short | 2 | 2 | 2
int | 4 | 4 | 4
long | 4 | 4 | 8
long long | 8 | 8 | 8
float | 4 | 4 | 4
double | 8 | 8 | 8
long double | 8 | 10/12 | 10/16
pointer | 4 | 4 | 8

## Slide 52: Unit of Main Memory Capacity
K:1KB= 210byte=1024byte
M:1MB= 220byte=1 048 576byte
G:1GB= 230byte=1 073 741 824byte
T:1TB= 240byte=1 099 511 627 776byte
P:1PB= 250byte=1 125 899 906 842 624byte
E:1EB= 260byte=1 152 921 504 606 846 976byte
Z:1ZB= 270byte=1 180 591 620 717 411 303 424 byte
Y:1YB= 280byte=1 208 925 819 614 629 174 706 176 byte

## Slide 53: Unit of Frequency and Line Width
b/s:bps
kb/s:1kb/s= 103b/s=1000bps
Mb/s:1Mb/s=106b/s=1000kbps
Gb/s:1Gb/s=109b/s=1000Mbps
Tb/s:1Tb/s=1012b/s=1000Gbps
Notes: 硬盘/文件大小相对混乱，2进制和10进制都出现过，IEC1998年给出二进制前缀字母定义，如KiB，MiB

## Slide 54: Data Storage and Arrangement Order
Least Significant Bit vs. Least Significant Byte
Most Significant Bit vs. Most Significant Byte
How should bytes within a multi-byte word be ordered in memory?
Conventions
  Big Endian: Sun, PPC Mac, Internet
    Least significant byte has highest address
  Little Endian: x86
    Least significant byte has lowest address
Notes: LSBit与MSBit的单位都是bit位，一个芯片的管脚中，对于一个多比特的信号（就是要搞清楚谁是最高位谁是最低位），比如32根的地址线，从低开始按0到31编个号。MSB就是31，LSB就是0。那么如果标记为：ADDR[31:0]就是MSB first的方式，如果标记为ADDR[0:31]就是LSB first的方式。LSB和MSB是以机器码为单位进行排序。
实际上，由于CPU存储数据操作的最小单位是一个字节，字节内部的比特序是什么样对我们的程序来说是一个黑盒子。

## Slide 55: Byte Ordering Example
Example
  Variable x has 4-byte representation 0x01234567
  Address given by &x is 0x100
0x100
0x101
0x102
0x103
01
23
45
67
0x100
0x101
0x102
0x103
67
45
23
01
Big Endian
Little Endian
01
23
45
67
67
45
23
01
Notes: 大端小端仅仅针对的是字节在内存中储存的顺序，和二进制bit顺序无关。

## Slide 56: Summary
Introduction to computer systems
Binary number representation
Arithmetic operations
Representation of numeric data
Representation of non-numeric data
Data width and storage