## Slide 1
Lei Wu
Zhejiang University
Computational Operations & Units

## Slide 2
Many images and resources used in this lecture are collected from the Internet, and they are used only for the educational purpose. The copyright belong to the original owners, respectively.
Part of slides credit to
  David Money Harris and Sarah L. Harris. Digital Design and Computer Architecture, 2nd Edition.
  Morris R. Mano , Charles R. Kime and Tom Martin. Logic & Computer Design Fundamentals, Fifth Edition.
  EECC 341, Prof. Muhammad Shaaban @ Rochester Institute of Technology
Disclaimer

## Slide 3: Overview
Basic computational units
Fixed number operations
  Addition & Subtraction
Arithmetic logic unit (ALU)
Fixed number operations
  Multiplication & Division

## Slide 4: Overview
Basic computational units
Fixed number operations
  Addition & Subtraction
Arithmetic logic unit (ALU)
Fixed number operations
  Multiplication & Division

## Slide 5: 1-Bit Adders
Notes: Cout = AB + (A^B)Cin

## Slide 6: Multibit Carry Propagate Adders (CPA)
Types of CPA
  Ripple-carry (slow)
  Carry-lookahead (fast)
  Prefix (faster)
Carry-lookahead and prefix adders faster for large adders but require more hardware
Symbol
Notes: CRA: 行波进位加法器（串行）
CLA：先行进位加法器（并行）
Prefix：前缀加法器
几乎所有的算术运算都要用到ALU，ALU的核心是加法器，所以加法器的速度是提高运算速度的关键。
串行有依赖关系，并行消除依赖关系。

## Slide 7: Ripple-Carry Adder (RCA)
Chain 1-bit adders together
Carry ripples through entire chain
Disadvantage: slow

## Slide 8: Ripple-Carry Adder Delay
tripple = NtFA
tFA: delay of a 1-bit full adder

## Slide 9: Carry-Lookahead Adder (CLA)
E.g., a 4-bit adder
  C1 = A0B0 + (A0 + B0) C0
  C2 = A1B1 + (A1 + B1) C1
  = A1B1 + (A1 + B1) A0B0 + (A1 + B1)(A0 + B0) C0
  C3 = A2B2 + (A2 + B2) C2
  = A2B2 + (A2 + B2) A1B1 + (A2 + B2)(A1 + B1)A0B0 + (A2 + B2)(A1 + B1)(A0 + B0) C0
  C4 = A3B3 + (A3 + B3) C3
  = A3B3 + (A3 + B3) A2B2 + (A3 + B3)(A2 + B2)A1B1 + (A3 + B3) (A2 + B2)(A1 + B1)A0B0 + (A3 + B3)(A2 + B2)(A1 + B1)(A0 + B0) C0
Notes: 观察一下进位的计算，由两部分构成：
AiBi进位生成：AiBi均为1，不管有无低位的进位输入，本位一定向高位产生进位；
Ai + Bi进位传递：AiBi有一个为1，若有低位进位输入，则一定被传递到高位；

## Slide 10: Carry-Lookahead Adder: Bit Level
Column i produces a carry out by either generating a carry out or propagating a carry in to the carry out
Generate (Gi) and propagate (Pi) signals for each column:
    Column i will generate a carry out if Ai AND Bi are both 1
    Gi = Ai Bi
    Column i will propagate a carry in to the carry out if Ai OR Bi is 1
    Pi = Ai + Bi
    The carry out of column i+1 (Ci+1) is:
    Ci+1 = Ai Bi + (Ai + Bi ) Ci
    = Gi + Pi Ci
    The sum of column i (Si) is:
Si = Ai Bi Ci = Pi Ci
Notes: 观察一下进位的计算，由两部分构成：
Gi进位生成函数
Pi进位传递函数
实现Ci逻辑表达式的电路称为先行进位部件，即CLU(Carry-Lookahead Unit)

## Slide 11: Revisit the 4-Bit Adder
Compute carry out (Cout) for 4-bit blocks using generate and propagate signals
  C1 = G0 + P0C0
  C2 = G1 + P1C1
  = G1 + P1 (G0 + P0C0)
  = G1 + P1G0 + P1 P0C0
  C3 = G2 + P2C2
  = G2 + P2 (G1 + P1G0 + P1P0C0)
  = G2 + P2G1 + P2P1G0 + P2P1P0C0
  C4 = G3 + P3C3
  = G3 + P3 (G2 + P2G1 + P2P1G0 + P2P1P0C0)
  = G3 + P3G2 + P3P2G1 + P3P2P1G0 + P3P2P1P0C0

## Slide 12: 4-Bit CLA
Partial full adder

## Slide 13: Carry-Lookahead Addition: Block/Group Level
The 4-bit CLA could be extended to more than four bits, however, in practice, due to limited gate fan-in, such extension is not feasible.
Instead, the concept is extended another level by considering group generate (G3-0) and group propagate (P3-0) functions:
  G3:0 = G3 + P3(G2 + P2(G1 + P1G0))
  P3:0 = P3P2P1P0
Using these two equations:
  C4 = G3 + P3G2 + P3P2G1+ P3P2P1G0 + P3P2P1P0 C0
  = G3:0 + P3:0C0
Thus, it is possible to have four 4-bit adders use one of the same carry lookahead circuit to speed up 16-bit addition.
Notes: 更多位数的加法器可以通过将更多的CLU和CLA串接起来实现，比如4位一组（块），组内位4位先行进位，组间串行进位。
可以扩展到多位构成的块：如果一个块在不考虑进位输入的情况下也能产生进位输出，称其产生进位；如果一个块在有进位输入时能产生进位，称其传播进位。
有如下定义：
Gi:j：第i位到第j位进位生成函数，产生一个进位的条件是最高位列产生一个进位或者如果最高位列传递进位而且之前的列产生了进位，如此类推；
Pi:j：第i位到第j位进位传递函数，传递条件是块中所有列都能传播进位。

## Slide 14: Carry-Lookahead Addition: Block/Group Level (cont’d)
Step 1: compute Gi and Pi for all columns
Step 2: compute G and P for k-bit blocks
Step 3: Cin propagates through each k-bit propagate/generate block
Generally, for 4-bit blocks
Gi:j = Gi + Pi (Gi-1 + Pi-1 (Gi-2 + Pi-2Gj )
Pi:j = PiPi-1Pi-2Pj
Cj+1 = Gi:j + Pi:jCj
E.g., 4-bit blocks (G3:0 and P3:0) :
G3:0 = G3 + P3(G2 + P2(G1 + P1G0))
P3:0 = P3P2P1P0
Notes: 更多位数的加法器可以通过将更多的CLU和CLA串接起来实现，比如4位一组（块），组内位4位先行进位，组间串行进位。
可以扩展到多位构成的块：如果一个块在不考虑进位输入的情况下也能产生进位输出，称其产生进位；如果一个块在有进位输入时能产生进位，称其传播进位。
有如下定义：
Gi:j：第j位到第i位进位生成函数，产生一个进位的条件是最高位列产生一个进位或者如果最高位列传递进位而且之前的列产生了进位，如此类推；
Pi:j：第j位到第i位进位传递函数，传递条件是块中所有列都能传播进位。

## Slide 15: 4-Bit CLA (ripple vs look ahead)
Partial full adder
C0 – C1 – C2 – C3 – C4
C0 –C4

## Slide 16: Carry-Lookahead Addition: Block/Group Level (cont’d)
Step 1: compute Gi and Pi for all columns
Step 2: compute G and P for k-bit blocks
Step 3: Cin propagates through each k-bit propagate/generate block
C4 = G3 + P3G2 + P3P2G1 + P3P2P1G0 + P3P2P1P0C0= G3:0+ P3:0C0
C8 = G7 + P7G6 + P7P6G5 + P7P6P5G4 + P7P6P5P4C4= G7:4+ P7:4C4
C12 = G11+P11G10+P11P10G9+P11P10P9G8+ P11P10P9P8C8= G11:8+ P11:8C8
C16 = G15+P15G14+P15P14G13+P15P14P13G12+P15P14P13P12C12= G15:12+ P15:12C12
Generally, for 4-bit blocks
Gi:j = Gi + Pi (Gi-1 + Pi-1 (Gi-2 + Pi-2Gj )
Pi:j = PiPi-1Pi-2Pj
Cj+1 = Gi:j + Pi:jCj
Notes: 更多位数的加法器可以通过将更多的CLU和CLA串接起来实现，比如4位一组（块），组内位4位先行进位，组间串行进位。
可以扩展到多位构成的块：如果一个块在不考虑进位输入的情况下也能产生进位输出，称其产生进位；如果一个块在有进位输入时能产生进位，称其传播进位。
有如下定义：
Gi:j：第i位到第j位进位生成函数，产生一个进位的条件是最高位列产生一个进位或者如果最高位列传递进位而且之前的列产生了进位，如此类推；
Pi:j：第i位到第j位进位传递函数，传递条件是块中所有列都能传播进位。

## Slide 17: 4-Bit Adder vs. 16-Bit Adder
C4 = G3:0+ P3:0C0
C8 = G7:4+ P7:4C4
C12 = G11:8+ P11:8C8
C16 = G15:12+ P15:12C12
C1 = G0+ P0C0
C2 = G1+ P1C1
C3 = G2+ P2C2
C4 = G3+ P3C3
4-bit Adder
16-bit Adder
Exactly the same structure. So CLA could be used to generate Group Carry.
Notes: 可以扩展到多位构成的块：
Gi:j：第i位到第j位进位生成函数，生成条件是最高位列产生一个进位或者如果最高位列传递进位而且之前的列产生了进位，如此类推；
Pi:j：第i位到第j位进位传递函数，传递条件是块中所有列都能传播进位。

## Slide 18: 32-bit CLA with 4-bit Blocks

## Slide 19: Carry-Lookahead Adder Delay
tCLA = tpg + tpg_block +(N/k - 1) tAND_OR + ktFA
tpg: delay to generate all PiGi
tpg_block: delay of generate all Pi:j, Gi:j
tAND_OR: delay from Cin to Cout of final AND/OR gate in k-bit CLA block

## Slide 20: Delay: RCA vs. CLA
Gate levels of Ci and Si
  RCA (2 and 1) vs. CLA (3 and 4)
Different metric types
  Only gate levels
    All gates share the same cost
  With specs
    Delay of typical gate X # of gate levels
    E.g.,
      Carry propagation delay: 12 ns
      Sum propagation delay: 15 ns
An N-bit carry-lookahead adder is generally much faster than a ripple-carry adder for N > 16

## Slide 21: Prefix Adder
Computes carry in (Ci-1) for each column, then computes sum:
Si = (Ai Bi) Ci-1
Computes G and P for 1-, 2-, 4-, 8-bit blocks, etc. until all Gi (carry in) known
log2N stages
Notes: 为进一步提高运算速度，可以采用组内和组间都并行的两级先行进位方式。

## Slide 22: Prefix Adder (cont’d)
Carry in either generated in a column or propagated from a previous column.
Column -1 holds Cin, so
G-1 = Cin, P-1 = 0
Carry in to column i == carry out of column i-1:
Ci-1 = Gi-1:-1
Gi-1:-1: generate signal spanning columns i-1 to -1
Sum equation:
Si = (Ai Bi) Gi-1:-1
Goal: Quickly compute G0:-1, G1:-1, G2:-1, G3:-1, G4:-1, G5:-1, … (called prefixes)

## Slide 23: Prefix Adder (cont’d)
Generate and propagate signals for a block spanning bits i:j:
Gi:j = Gi:k + Pi:k Gk-1:j
Pi:j = Pi:kPk-1:j
In words:
  Generate: block i:j will generate a carry if:
    upper part (i:k) generates a carry or
    upper part propagates a carry generated in lower part (k-1:j)
  Propagate: block i:j will propagate a carry if both the upper and lower parts propagate the carry

## Slide 24: Prefix Adder Schematic

## Slide 25: Prefix Adder Delay
tPA = tpg + log2N(tpg_prefix) + tXOR
tpg: delay to produce PiGi (AND or OR gate)
tpg_prefix: delay of black prefix cell (AND-OR gate)

## Slide 26: Half Subtractor
Subtracting a single-bit binary value Y from anther X (i.e., X -Y ) produces a difference bit D and a borrow out bit B-out.
This operation is called half subtraction and the circuit to realize it is called a half subtractor.
X
0
0
1
1
Y
0
1
0
1
D
0
1
1
0
B-out
0
1
0
0
Half Subtractor Truth Table
Inputs
Outputs
  D = X’Y + XY’
  = X Å Y
  B-out = X’Y
Half
Subtractor
X
Y
D
B-OUT
X
Y
Difference D
B-out
Notes: HS vs. HA

## Slide 27: Full Subtractor
Subtracting two single-bit binary values, Y, B-in from a single-bit value X produces a difference bit D and a borrow out B-out bit. This is called full subtraction.
X
0
0
0
0
1
1
1
1
Y
0
0
1
1
0
0
1
1
D
0
1
1
0
1
0
0
1
B-out
0
1
1
1
0
0
0
1
B-in
0
1
0
1
0
1
0
1
Full Subtractor Truth Table
  D(X,Y, Bin) = S (1,2,4,7)
  Bout(X, Y, Bin) = S (1,2,3,7)
Inputs
Outputs
Difference D
Bin
X
0
1
00 01 11 10
Y
Bin
XY
0
1
2
3
6
7
4
5
1
1
1
1
Bin
X
0
1
00 01 11 10
Y
Bin
XY
0
1
2
3
6
7
4
5
1
1
1
1
Borrow Bout
D = X’Y’(Bin) + XY’(Bin)’ + XY’(Bin)’ + XY(Bin)
D = X Å Y Å (Bin)
Bout = X’Y + X’(Bin) + Y(Bin)
Notes: FS vs. FA
全加器进位
全减器借位

## Slide 28: Full Subtractor Circuit Using AND-OR
X’Y
YBin
Bout
X’Bin
X’
X’
Y
B-in
Y
B-in
Y
Y’
Y
X
X’
X
Bin
Bin’
Bin
X’Y’Bin
XY’Bin’
Difference D
X’YBin’
XYBin
X’
X’
X
X
Y’
Y
Y
B-in
Y
B-in’
B-in’
B-in’
Full
Subtractor
X
Y
D
Bin
Bout

## Slide 29: Circuit Using XOR

## Slide 30: Implementation of N-bit Subtractors
An n-bit subtractor used to subtract an n-bit number Y from another n-bit number X (i.e., X-Y) can be built in one of two ways:
  By using n full subtractors and connecting them in series, creating a borrow ripple subtractor:
    Each borrow out B-out from a full subtractor at position j is connected to the borrow in B-in of the full subtractor at the higher position j+1.
  By using an n-bit adder and n inverters:
    Find 2’s complement of Y by:
      Inverting all the bits of Y using the n inverters.
      Adding 1 by setting the carry in of the least significant position to 1
    The original subtraction (X - Y) now becomes an addition of X to two’s complement of Y using the n-bit adder.
Notes: 2’s complement实现加减法统一

## Slide 31: 4-bit Borrow Ripple Subtractor
Subtracts two 4-bit numbers:
Y = Y3 Y2 Y1 Y0 from
X = X3 X2 X1 X0
  producing the difference D = D3 D2 D1 D0 , Bout = B4 from the most significant position j=3
4-bit
Subtractor
X3X2X1X0
D3 D2 D1 D0
Bin
Bout
B4
Y3Y2Y1Y0
B0 =0
Inputs
Difference Output D
Full
Subtractor
X1
Y1
D1
Bin
Bout
X0
Y0
D0
Bin
Bout
B0 =0
X2
Y2
D2
Bin
Bout
X3
Y3
D3
Bin
Bout
B1
B2
B3
B4
Data inputs to be subtracted
Difference output D
Full
Subtractor
Full
Subtractor
Full
Subtractor

## Slide 32: 4-bit Subtractor Using 4-bit Adder
4-bit
Adder
X3 X2 X1 X0
D3 D2 D1 D0
C-in
C-out
C4
Y3 Y2 Y1 Y0
C0 = 1
Inputs to be subtracted
Difference Output
S3 S2 S1 S0

## Slide 33: Overview
Basic computational units
Fixed number operations
  Addition & Subtraction
Arithmetic logic unit (ALU)
Fixed number operations
  Multiplication & Division

## Slide 34: 4-Bit Binary Adder-Subtractors
When S=0: Addition (A+B)
When S=1: Subtraction (A+2’s complement of B)
Can be used to add/subtract unsigned numbers and signed 2’s complement numbers

## Slide 35: Addition/Subtraction
Both can be handled by using 2’s complement representation
Can achieve a unified implementation
  Addition vs. subtraction
  Unsigned vs. signed
Corner cases shall be considered
  Some important flags

## Slide 36: Carry & Overflow
Carry is important when…
  Adding or subtracting unsigned integers
  Indicates that the unsigned sum is out of range
  Either < 0 or > maximum unsigned n-bit value
Overflow is important when…
  Adding or subtracting signed integers
  Indicates that the signed sum is out of range
Overflow occurs when?
Notes: 广义来讲，carry可被视为unsigned number的overflow
In unsigned magnitude addition
  A carry out of the left-most bit is also an overflow
In unsigned magnitude subtraction
  Overflow will occur in subtraction if we must borrow prior to the left-most bit

## Slide 37: Signed Overflow
With two’s complement and a 4-bit adder, for example, the largest representable decimal number is +7, and the smallest is -8.
What if you try to compute 4 + 5, or (-4) + (-5)?
We cannot just include the carry out to produce a five-digit result, as for unsigned addition. If we did, (-4) + (-5) would result in +23!
Also, unlike the case with unsigned numbers, the carry out cannot be used to detect overflow, by itself
  In the example on the left, the carry out is 0 but there is overflow.
  Conversely, there are situations where the carry out is 1 but there is no overflow.
0 1 0 0 (+4)
+ 0 1 0 1 (+5)
0 1 0 0 1 (-7)
1 1 0 0 (-4)
+ 1 0 1 1 (-5)
1 0 1 1 1 (+7)

## Slide 38: How to Detect Signed Overflow?
The impact of carry and overflow
The easiest way to detect signed overflow is to look at all the sign bits.
0 1 0 0 (+4)
+ 0 1 0 1 (+5)
0 1 0 0 1 (-7)
1 1 0 0 (-4)
+ 1 0 1 1 (-5)
1 0 1 1 1 (+7)
Examples of four signed additions
Notes: 1111 + 0001 = 0000 should set carry (15 + 1 = 0 is false) and clear overflow (-1 + 1 = 0 is true).
0111 + 0010 = 1001 should clear carry (7 + 2 = 9 is true) and set overflow (7 + 2 = -7 is false).
1001 + 1001 = 0010 should set both (9 + 9 = 2 and -7 + -7 = 2 are both false).

## Slide 39: Detecting Signed Overflow
Overflow occurs only in the two situations:
  Adding two positive numbers and the sum is negative
  Adding two negative numbers and the sum is positive
  Can happen because of the fixed number of sum bits
Overflow cannot occur if you add a positive number to a negative number. Do you see why?
In two’s complement addition/subtraction
  If the two numbers have the same sign bit and the sum/difference has a different sign bit, then overflow
  Or, if the carry out flags of the sign bit and the highest value bit are different

## Slide 40: Important Flags
Zero flag (ZF)
  ZF = 1 means the result is 0
  Valid for both unsigned and signed operations
Sign flag (SF/NF)
  The sign of the result, i.e., Sn-1
  Valid for signed operations
Carry/borrow flag (CF)
  If CF = 1
    Carry for addition, i.e., Cout
    Borrow for subtraction, i.e., ~Cout
  Valid for unsigned operations
Overflow flag (OF)
  Valid for signed operations
Notes: 零标志：ZF = 1 if and only if S = 0
符号标志：SF= Sn-1
进位/借位标志：CF = Cout ^ Cin，即Cin=0时，CF为进位Cout；反之，CF为进位Cout取反。
溢出标志：OF = Cout ^ Cn-1
Cout即Cn

## Slide 41: Adders with Flags
ZF, SF, CF and OF
Symbol
ZF
OF
CF
SF
Notes: 零标志：ZF = 1 if and only if S = 0
符号标志：SF= Sn-1
进位/借位标志：CF = Cout ^ Cin，即Cin=0时，CF为进位Cout；反之，CF为进位Cout取反。
溢出标志：OF = Cout ^ Cn-1
Cout即Cn