## Slide 1
Lei Wu
Zhejiang University
Computational Operations & Units

## Slide 2
Many images and resources used in this lecture are collected from the Internet, and they are used only for the educational purpose. The copyright belong to the original owners, respectively.
Part of slides credit to
  David Money Harris and Sarah L. Harris. Digital Design and Computer Architecture, 2nd Edition.
  Morris R. Mano , Charles R. Kime and Tom Martin. Logic & Computer Design Fundamentals, Fifth Edition.
  ECE 142, Prof. Jun Yang @ Univ. of Pittsburgh
  ECE/CS 552, Prof. Mikko Lipasti @ Univ. of Wisconsin
Disclaimer

## Slide 3: Overview
Basic computational units
Fixed number operations
  Addition & Subtraction
Arithmetic logic unit (ALU)
Fixed number operations
  Multiplication & Division

## Slide 4: Datapath and ALU
The datapath and the control unit are the two parts of the processor, or CPU, of a computer.
Instead of having each individual register perform its microoperations directly, computer systems often employ many storage registers in conjunction with a shared operation unit called an arithmetic/logic unit, abbreviated ALU.
  To perform a microoperation, the contents of specified source registers are applied to the inputs of the shared ALU. The ALU performs an operation, and the result of this operation is transferred to a destination register.

## Slide 5: What is ALU?
An arithmetic-logic unit, or ALU, performs many different arithmetic and logic operations. The ALU is the “heart” of a processor—you could say that everything else in the CPU is there to support the ALU.
Notes: ALU是一种能进行多种算术运算与逻辑运算的组合逻辑电路，核心部件是带标志位加法器，多采用先行进位方式。
F：ALU flags，即OF、SF、ZF and CF
关于符号位，如溢出（OF）和进位（借位，CF）。

## Slide 6: Datapath = ALU + Registers
The combination of a set of registers with a shared ALU and interconnecting paths is the datapath for the system.
The control unit for the datapath directs the information low through the buses, the ALU, the shifter, and the registers by applying signals to the select inputs.
Notes: Each register is connected to two multiplexers to form ALU and shifter input buses A and B. The select inputs on each multiplexer select one register for the corresponding bus. For Bus B, there is an additional multiplexer, MUX B, so that constants can be brought into the datapath from outside using Constant in. Bus B also connects to Data out, to send data outside the datapath to other components of the system, such as memory or input–output. Likewise, Bus A connects to Address out, to send address information outside of the datapath for memory or input–output.
The sets of values must be generated and must become available on the corresponding control lines early in the clock cycle. The binary data from the two source registers must propagate through the multiplexers and the ALU and on into the inputs of the destination register, all during the remainder of the same clock cycle. Then, when the next positive clock edge arrives, the binary data on Bus D is loaded into the destination register. To achieve fast operation, the ALU and shifter are con- structed with combinational logic having a limited number of levels.

## Slide 7: ALU in the Datapath
With the ALU as a combinational circuit, the entire register transfer operation from the source registers, through the ALU, and into the destination register is performed during one clock cycle.
  The shift operations are often performed in a separate unit, but sometimes these operations are also implemented within the ALU.
Notes: Arithmetic and logic microoperations are performed on the operands on the A and B buses by the ALU. The G select inputs select the microoperation to be per- formed by the ALU. The shift microoperations are performed on data on Bus B by the shifter. The H select input either passes the operand on Bus B directly through to the shifter output or selects a shift microoperation. MUX F selects the output of the ALU or the output of the shifter. MUX D selects the output of MUX F or external data on input Data in to be applied to Bus D. The latter is connected to the inputs of all the registers. The destination select inputs determine which register is loaded with the data on Bus D. Since the select inputs are decoded, only one register Load signal is active for any transfer of data into a register from Bus D. A Load enable signal that can force all register Load signals to 0 using AND gates is present for transfers that are not to change the contents of any of the four registers.

## Slide 8: How to Design An ALU
We perform the design of this ALU in three stages
  Design the arithmetic section
  Design the logic section
  Combine the above two sections to form the ALU
Notes: A typical n-bit ALU. The n data inputs from A are combined with the n data inputs from B to generate the result of an operation at the G outputs. The mode-select input S2 distinguishes between arithmetic and logic operations. The two Operation select inputs S1 and S0 and the Carry input Cin specify the eight arithmetic operations with S2 at 0. Operand select input S0 and Cin specify the four logic operations with S2 at 1.

## Slide 9: A Simple Example: 1-Bit ALU with 3 OPs
module ALU(
input [3:0] a, b,
input [1:0] aluop,
input cin,
output [3:0] f,
output OF, SF, ZF, CF,
output cout
);
wire [3:0] sum;
CLA_FLAGS(a, b, cin, sum, OF, SF, ZF, CF, cout);
always @(*) begin
case(aluop)
2’b00: f = a & b;
2’b01: f = a | b;
2’b10: f = sum;
default: f = 0;
endcase
end
endmodule
F1:0 | Function
00 | A & B
01 | A ¦ B
10 | A + B
11 | not used
Notes: The ALU is a combinational circuit that performs a set of basic arithmetic and logic microoperations. It has a number of selection lines used to determine the operation to be performed. The selection lines are decoded within the ALU, so that k selection lines can specify up to 2k distinct operations.
default分支很重要，否则，综合器将会综合处锁存器，违反ALU组合逻辑电路的特性。
ALU中也可以实现左（右）移位操作，或者用专门的移位寄存器实现。多位（>2）的移位通常用ALU之外的桶形移位器实现，利用大量的多路选择器实现快速移位。

## Slide 10: N-Bit ALU with 8 OPs
F2:0 | Function
000 | A & B
001 | A ¦ B
010 | A + B
011 | not used
100 | A & ~B
101 | A ¦ ~B
110 | A - B
111 | SLT
Notes: SLT：Set Less Than, see next page

## Slide 11: Set Less Than (SLT) Example
Configure 32-bit ALU for SLT operation: A = 25 and B = 32
  A < B, so Y should be 32-bit representation of 1 (0x00000001)
  F2:0 = 111
    F2 = 1 (adder acts as subtracter), so 25 - 32 = -7
    -7 has 1 in the most significant bit (S31 = 1)
    F1:0 = 11 multiplexer selects Y = S31 (zero extended) = 0x00000001.
Notes: 最高位0扩展

## Slide 12: Various Use of Shifters
Logical shifter: shifts value to left or right and fills empty spaces with 0’s
  11001 >> 2 = 00110
  11001 << 2 = 00100
Arithmetic shifter: same as logical shifter, but on right shift, fills empty spaces with the old most significant bit (MSB).
  11001 >>> 2 = 11110
  11001 <<< 2 = 00100
Rotator: rotates bits in a circle, such that bits shifted off one end are shifted into the other end
  11001 ROR 2 = 01110
  11001 ROL 2 = 00111

## Slide 13: Shifters as Multipliers and Dividers
A << N = A × 2N
  E.g., 00001 << 2 = 00100 (1 × 22 = 4)
  E.g., 11101 << 2 = 10100 (-3 × 22 = -12)
A >>> N = A ÷ 2N
  E.g., 01000 >>> 2 = 00010 (8 ÷ 22 = 2)
  E.g., 10000 >>> 2 = 11100 (-16 ÷ 22 = -4)

## Slide 14: Recall the Design of A Shifter
Bidirectional shift registers with parallel load
  Data from Bus B can be transferred to the register in parallel and then shifted to the right, the left, or not at all.
  A clock pulse loads the output of Bus B into the shift register, and a second clock pulse performs the shift.
  Finally, a third clock pulse transfers the data from the shift register to the selected destination register.
Alternatively, the transfer from a source register to a destination register can be done using only one clock pulse if the shifter is implemented as a combinational circuit
  Because of the faster operation that results from the use of one clock pulse instead of three, this is the preferred method.
  In a combinational shifter, the signals propagate through the gates without the need for a clock pulse.
  Hence, the only clock needed for a shift in the datapath is for loading the data from Bus H into the selected destination register.

## Slide 15: Shifter Design as A Combinational Circuit
Notes: 4-Bit Basic Shifter

## Slide 16: 4-Bit Barrel Shifter (ROL)

## Slide 17: Overview
Basic computational units
Fixed number operations
  Addition & Subtraction
Arithmetic logic unit (ALU)
Fixed number operations
  Multiplication & Division
Multiplication is vexation, Division is as bad;
The rule of three doth puzzle me, And practice drives me mad.
--- Anonymous, Elizabethan manuscript, 1570

## Slide 18: Fixed number operations
Addition/subtraction
Multiplication
Division

## Slide 19: Multiplication
More complicated than addition
  A straightforward implementation will involve shifts and adds
More complex operation can lead to
  More area (on silicon) and/or
  More time (multiple cycles or longer clock cycle time)
Let’s begin from a simple, straightforward method

## Slide 20: Decimal vs. Binary Multiplication
Partial products formed by multiplying a single digit of the multiplier with multiplicand
Shifted partial products summed to form result

## Slide 21: Unsigned Multiplication: 4-bit X 4-bit

## Slide 22: Unsigned Multiplication: M-bit X N-bit
A＝am－1…a1a0 B＝bn－1…b1b0

## Slide 23: Straightforward Algorithm
01010010 (multiplicand)
01101101 (multiplier)
x
01010010
00000000
01010010
01010010
00000000
01010010
01010010
00000000
010001011101010
Notes: 手算的特点：
用乘数的每一位依次乘以被乘数得到X x Yi，如果Yi = 0，则得到0；否则得到X；
把1中求得的各项结果逐次左移，而后求和。

## Slide 24: How to Revise it?
01010010 (multiplicand)
01101101 (multiplier)
x
000000000000000 (partial sum)
Notes: 为了效率考虑，可以做如下改进：
每次将乘数的一位乘以被乘数后（X x Yi），将结果与前面所得累加，称为为部分积；
对乘数中为1的位执行加法和右移运算，对为0的位只执行右移运算，不需执行加法运算。

## Slide 25: How to Revise it?
01010010 (multiplicand)
01101101 (multiplier)
x
000000001010010 (partial sum)

## Slide 26: How to Revise it?
000000001010010 (partial sum)
01010010 (multiplicand)
01101101 (multiplier)
x
00000000

## Slide 27: How to Revise it?
000000001010010 (partial sum)
01010010 (multiplicand)
01101101 (multiplier)
x

## Slide 28: How to Revise it?
000000001010010 (partial sum)
01010010 (multiplicand)
01101101 (multiplier)
x
01010010

## Slide 29: How to Revise it?
01010010 (multiplicand)
01101101 (multiplier)
x
000000110011010 (partial sum)

## Slide 30: How to Revise it?
000000110011010 (partial sum)
01010010 (multiplicand)
01101101 (multiplier)
x
01010010

## Slide 31: How to Revise it?
01010010 (multiplicand)
01101101 (multiplier)
x
000010000101010 (partial sum)

## Slide 32: How to Revise it?
000010000101010 (partial sum)
01010010 (multiplicand)
01101101 (multiplier)
x
00000000

## Slide 33: How to Revise it?
01010010 (multiplicand)
01101101 (multiplier)
x
000010000101010 (partial sum)

## Slide 34: How to Revise it?
000010000101010 (partial sum)
01010010 (multiplicand)
01101101 (multiplier)
x
01010010

## Slide 35: How to Revise it?
01010010 (multiplicand)
01101101 (multiplier)
x
000111001101010 (partial sum)

## Slide 36: How to Revise it?
01010010 (multiplicand)
01101101 (multiplier)
x
01010010
000111001101010 (partial sum)

## Slide 37: How to Revise it?
01010010 (multiplicand)
01101101 (multiplier)
x
010001011101010 (partial sum)

## Slide 38: How to Revise it?
010001011101010 (partial sum)
01010010 (multiplicand)
01101101 (multiplier)
x
00000000

## Slide 39: How to Revise it?
010001011101010 (full sum)
01010010 (multiplicand)
01101101 (multiplier)
x

## Slide 40: Implementation 1
Notes: 需要多个时钟周期完成，属于时序逻辑电路，由时钟信号控制。

## Slide 41: Example of Implementation 1
Let’s do 0010 x 0110 (2 x 6), unsigned
Iteration | Implementation 1 |  |  | 
 | Step | Multiplier | Multiplicand | Product
0 | initial values | 0110 | 0000 0010 | 0000 0000
1 | 1: 0 -> no op | 0110 | 0000 0010 | 0000 0000
 | 2: Multiplier shift right/ Multiplicand shift left | 011 | 0000 0100 | 0000 0000
2 | 1: 1 -> product = product + multiplicand | 011 | 0000 0100 | 0000 0100
 | 2: Multiplier shift right/ Multiplicand shift left | 01 | 0000 1000 | 0000 0100
3 | 1: 1 -> product = product + multiplicand | 01 | 0000 1000 | 0000 1100
 | 2: Multiplier shift right/ Multiplicand shift left | 0 | 0001 0000 | 0000 1100
4 | 1: 0 -> no op | 0 | 0001 0000 | 0000 1100
 | 2: Multiplier shift right/Multiplicand shift left |  | 0010 0000 | 

## Slide 42: Drawbacks
The ALU is twice as wide as necessary
The multiplicand register takes twice as many bits as needed
The product register won’t need 2n bits till the last step
  Being filled
The multiplier register is being emptied during the process

## Slide 43: Implementation 2
Multiplicand stationary - Multiplier right - PP right
Notes: 计算机中为了提高效率，做了如下改进：
每次将乘数的一位乘以被乘数后（X x Yi），将结果与前面所得累加，称为为部分积；
对乘数中为1的位执行加法和右移运算，对为0的位只执行右移运算，不需执行加法运算；
每次求得X x Yi后，不是将它左移与前次部分积相加，而是将部分积右移一位与X x Yi相加。

## Slide 44: Example of Implementation 2
Let’s do 0010 x 0110 (2 x 6), unsigned
Iteration | Implementation 2 |  |  | 
 | Step | Multiplier | Multiplicand | Product
0 | initial values | 0110 | 0010 | 0000 ××××
1 | 1: 0 -> no op | 0110 | 0010 | 0000 ××××
 | 2: Multiplier shift right/ Product shift right | ×011 | 0010 | 0000 0×××
2 | 1: 1 -> product = product + multiplicand | ×011 | 0010 | 0010 0×××
 | 2: Multiplier shift right/ Product shift right | ××01 | 0010 | 0001 00××
3 | 1: 1 -> product = product + multiplicand | ××01 | 0010 | 0011 00××
 | 2: Multiplier shift right/ Product shift right | ×x×0 | 0010 | 0001 100×
4 | 1: 0 -> no op | ×××0 | 0010 | 0001 100×
 | 2: Multiplier shift right/ Product shift right | ×××× | 0010 | 0000 1100

## Slide 45: Implementation 3
Multiplier on right half of PP reg
Multiplicand stationary - Multiplier right - PP right

## Slide 46: Example of Implementation 3
Let’s do 0010 x 0110 (2 x 6), unsigned
Iteration | Implementation 3 |  |  | 
 | Step | Multiplier | Multiplicand | Product¦Multiplier
0 | initial values | 0110 | 0010 | 0000 0110
1 | 1: 0 -> no op | 0110 | 0010 | 0000 0110
 | 2: Multiplier shift right/ Product shift right | ×011 | 0010 | 0000 0011
2 | 1: 1 -> product = product + multiplicand | ×011 | 0010 | 0010 0011
 | 2: Multiplier shift right/ Product shift right | ××01 | 0010 | 0001 0001
3 | 1: 1 -> product = product + multiplicand | ××01 | 0010 | 0011 0001
 | 2: Multiplier shift right/ Product shift right | ××00 | 0010 | 0001 1000
4 | 1: 0 -> no op | ×××0 | 0010 | 0001 1000
 | 2: Multiplier shift right/ Product shift right | ×××× | 0010 | 0000 1100

## Slide 47: Signed Multiplication
Recall
  For p = a x b, if a < 0 or b < 0, then p < 0
  If a < 0 and b < 0, then p > 0
  Hence sign(p) = sign(a) xor sign(b)
Hence
  Convert multiplier, multiplicand to positive number with (n-1) bits
  Multiply positive numbers
  Compute sign, convert product accordingly
  Or, Perform sign-extension on shifts for prev. design

## Slide 48: Multiplication
1 0001
4 x 0100
0000
0000
0001
0000 0
xxxxxxxx
4 00000100
-7 1001
4 x 0100
0000
0000
111001
0000 0
xxxxxxxx
-28 11100100
1 0001
-4 x 1100
0000
0000
0001
11111 0
xxxxxxxx
-4 11111100
-7 1001
-4 x 1100
00000000
0000000
111001
00111 0 (符号位1，同上)
xxxxxxxx
28 100011100
符号位1，我们取反+1：0001->1110->1111，
高位补齐，低位添0
->（1）1111(000)

## Slide 49: Example of Signed Multiplication
Note:
  Sign extension of partial product
  If most significant bit of multiplier is 1, then subtract
→
+
+
→
+
→
→
→
+
→
→
→
→
+
→
→
→
+
+
+
→
→
→
→
111111001
000111
1000110001

## Slide 50: Booth’s Encoding
Recall grade school trick
  When multiplying by 9:
    Multiply by 10 (easy, just shift digits left)
    Subtract once
  E.g.
    123454 x 9 = 123454 x (10 – 1) = 1234540 – 123454
    Converts addition of six partial products to one shift and one subtraction
Booth’s algorithm applies same principle
  Except no ‘9’ in binary, just ‘1’ and ‘0’
  So, it’s actually easier!

## Slide 51: Booth’s Encoding
Search for a run of ‘1’ bits in the multiplier
  E.g., ‘0110’ has a run of 2 ‘1’ bits in the middle
  Multiplying by ‘0110’ (6 in decimal) is equivalent to multiplying by 8 and subtracting twice, since 6 x m = (8 – 2) x m = 8m – 2m
Hence, iterate right to left and:
  Subtract multiplicand from product at first ‘1’
  Add multiplicand to product after last ‘1’
  Don’t do either for ‘1’ bits in the middle

## Slide 52: Booth’s Encoding
Really just a new way to encode numbers
  Normally positionally weighted as 2n
  With Booth, each position has a sign bit
  Can be extended to multiple bits
0 | 1 | 1 | 0 | Binary
+1 | 0 | -1 | 0 | 1-bit Booth
+2 |  | -2 |  | 2-bit Booth
Yj | Yj-1 | 1-bit Encoding
0 | 0 | +0
0 | 1 | +1
1 | 0 | -1
1 | 1 | -0
Yj+1 | Yj | Yj-1 | 2-bit Encoding
0 | 0 | 0 | +0
0 | 0 | 1 | +1
0 | 1 | 0 | +1
0 | 1 | 1 | +2
1 | 0 | 0 | -2
1 | 0 | 1 | -1
1 | 1 | 0 | -1
1 | 1 | 1 | -0
检测连续的1
111…1 = 2n-1，类比9，999

## Slide 53: Booth’s Algorithm
Current bit | Bit to right | Explanation | Example | Operation
1 | 0 | Begins run of ‘1’ | 00001111000 | Subtract
1 | 1 | Middle of run of ‘1’ | 00001111000 | Nothing
0 | 1 | End of a run of ‘1’ | 00001111000 | Add
0 | 0 | Middle of a run of ‘0’ | 00001111000 | Nothing
检测连续的1
111…1 = 2n-1，类比9，999

## Slide 54: Example 1 of Booth’s Algorithm
Let’s do 0010 x 1101 (2 x -3)
Iteration | Implementation 3 |  | 
 | Step | Multiplicand | Product
0 | initial values | 0010 | 0000 1101 0
1 | 10 -> product = product – multiplicand | 0010 | 1110 1101 0
 | shift right |  | 1111 0110 1
2 | 01 -> product = product + multiplicand | 0010 | 0001 0110 1
 | shift right |  | 0000 1011 0
3 | 10 -> product = product – multiplicand | 0010 | 1110 1011 0
 | shift right |  | 1111 0101 1
4 | 11 -> no op | 0010 | 1111 0101 1
 | shift right |  | 1111 1010 1
Notes: 0000-0010 = 1110

## Slide 55: Example 2 of Booth’s Algorithm
Negative multiplicand:
  -6 x 6 = -36
  1010 x 0110, 0110 in Booth’s encoding is +0-0
  Hence:
1111 1010 | x 0 | 0000 0000
1111 0100 | x –1 | 0000 1100
1110 1000 | x 0 | 0000 0000
1101 0000 | x +1 | 1101 0000
 | Final Sum: | 1101 1100 (-36)

## Slide 56: Example 3 of Booth’s Algorithm
Negative multiplier:
  -6 x -2 = 12
  1010 x 1110, 1110 in Booth’s encoding is 00-0
  Hence:
1111 1010 | x 0 | 0000 0000
1111 0100 | x –1 | 0000 1100
1110 1000 | x 0 | 0000 0000
1101 0000 | x 0 | 0000 0000
 | Final Sum: | 0000 1100 (12)

## Slide 57: 2-bits/cycle Booth Multiplier
For every pair of multiplier bits
  If Booth’s encoding is ‘-2’
    Shift multiplicand left by 1, then subtract
  If Booth’s encoding is ‘-1’
    Subtract
  If Booth’s encoding is ‘0’
    Do nothing
  If Booth’s encoding is ‘1’
    Add
  If Booth’s encoding is ‘2’
    Shift multiplicand left by 1, then add

## Slide 58: 2 bits/cycle Booth’s
Current | Previous | Operation | Explanation
00 | 0 | +0;shift 2 | [00] => +0, [00] => +0; 2x(+0)+(+0)=+0
00 | 1 | +M; shift 2 | [00] => +0, [01] => +M; 2x(+0)+(+M)=+M
01 | 0 | +M; shift 2 | [01] => +M, [10] => -M; 2x(+M)+(-M)=+M
01 | 1 | +2M; shift 2 | [01] => +M, [11] => +0; 2x(+M)+(+0)=+2M
10 | 0 | -2M; shift 2 | [10] => -M, [00] => +0; 2x(-M)+(+0)=-2M
10 | 1 | -M; shift 2 | [10] => -M, [01] => +M; 2x(-M)+(+M)=-M
11 | 0 | -M; shift 2 | [11] => +0, [10] => -M; 2x(+0)+(-M)=-M
11 | 1 | +0; shift 2 | [11] => +0, [11] => +0; 2x(+0)+(+0)=+0
1 bit Booth | 
00 | +0
01 | +M;
10 | -M;
11 | +0

## Slide 59: Why It Works?
Booth's algorithm performs an addition when it encounters the first digit of a block of ones (0 1) and a subtraction when it encounters the end of the block (1 0).
When the ones in a multiplier are grouped into long blocks, Booth's algorithm performs fewer additions and subtractions than the normal multiplication algorithm.
b × (a31a30….a0)
= a0 × b × 20 +
a1 × b × 21 +
…
a31 × b × 231
= ( 0 – a0 ) × b × 20 +
( a0 – a1) × b × 21 +
…
(a30 – a31) × b × 231 +
a31 × b × 232
Notes: a: multiplier
b: multiplicand

## Slide 60: Why It Works?
Works for positive multiplier coz a31 is 0
What happens for negative multipliers? a31 is 1
  Remember that we are using 2’s complement binary
b × (a31a30….a0) = b × (- a31 × 231+a30 × 230+….a0 ×20)
Same derivation applies

## Slide 61: Summary
Benefit: Reducing the number of partial products
Take away: Booth encoding

## Slide 62: Exercise
Signed Multiplication: x=5, y=-7
Unsigned Multiplication: x=5, y=3

## Slide 63: Yet Another Option: Array Multiplier
Adding all partial products simultaneously using an array of basic cells
 |  |  |  | 1 | 0 | 0 | 0
 |  |  | x | 1 | 0 | 0 | 1
 |  |  |  | 1 | 0 | 0 | 0
 |  |  | 0 | 0 | 0 | 0 | 
 |  | 0 | 0 | 0 | 0 |  | 
 | 1 | 0 | 0 | 0 |  |  | 
 | 1 | 0 | 0 | 1 | 0 | 0 | 0
Full Adder
Sin Cin Ai Bj
Cout Sout
Ai ,Bj
Notes: 采用硬件叠加或者流水处理的快速乘法器，如阵列乘法器，实现了手算的功能。

## Slide 64: 4 x 4 Array Multiplier
Notes: 采用硬件叠加或者流水处理的快速乘法器，如阵列乘法器，实现了手算的功能。

## Slide 65: 16-bit Array Multiplier
Conceptually straightforward
Fairly expensive hardware, integer multiplies relatively rare
  Most used in array address calc: replace with shifts
Notes: 基于CRA，可优化：
1）CSA：carry save adder，进位保留加法器，本级进位与本级和同时输出至下一级, O(n)；
2）Wallace Tree：WT，华莱士树，适用于16位以上的乘法，O(log(n))

## Slide 66: Fixed number operations
Addition/subtraction
Multiplication
Division

## Slide 67: Unsigned Division
Again, back to 3rd grade (74 ÷ 8 = 9 rem 2)
 |  |  |  |  |  |  |  | 1 | 0 | 0 | 1 | Quotient
Divisor | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 0 | Dividend
 |  |  |  | - | 1 | 0 | 0 | 0 |  |  |  | 
 |  |  |  |  |  |  |  | 1 | 0 |  |  | 
 |  |  |  |  |  |  |  | 1 | 0 | 1 |  | 
 |  |  |  |  |  |  |  | 1 | 0 | 1 | 0 | 
 |  |  |  |  |  |  | - | 1 | 0 | 0 | 0 | 
 |  |  |  |  |  |  |  |  |  | 1 | 0 | Remainder
Notes: Even more complicated
Can be accomplished via shifting and addition/subtraction
Negative numbers: Even more difficult
There are better techniques, we won’t look at them
类似部分积：中间余数
如果中间余数<除数，则中间余数不变
除数右移

## Slide 68: Unsigned Division
How does hardware know if division fits?
  Condition: if remainder ≥ divisor
  Use subtraction: (remainder – divisor) ≥ 0
OK, so if it fits, what do we do?
  Remaindern+1 = Remaindern – divisor
What if it doesn’t fit?
  Have to restore original remainder
Called restoring division
Notes: restoring division:恢复余数除法

## Slide 69: Implementation 1
 |  |  |  |  |  |  |  | 1 | 0 | 0 | 1 | Quotient
Divisor | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 0 | Dividend
 |  |  |  | - | 1 | 0 | 0 | 0 |  |  |  | 
 |  |  |  |  |  |  |  | 1 | 0 |  |  | 
 |  |  |  |  |  |  |  | 1 | 0 | 1 |  | 
 |  |  |  |  |  |  |  | 1 | 0 | 1 | 0 | 
 |  |  |  |  |  |  | - | 1 | 0 | 0 | 0 | 
 |  |  |  |  |  |  |  |  |  | 1 | 0 | Remainder
1. Place dividend in lower half
3. Get remainder here
2. Do the division

## Slide 70: Implementation 1
 |  |  |  |  |  |  |  | 1 | 0 | 0 | 1 | Quotient
Divisor | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 0 | Dividend
 |  |  |  | - | 1 | 0 | 0 | 0 |  |  |  | 
 |  |  |  |  |  |  |  | 1 | 0 |  |  | 
 |  |  |  |  |  |  |  | 1 | 0 | 1 |  | 
 |  |  |  |  |  |  |  | 1 | 0 | 1 | 0 | 
 |  |  |  |  |  |  | - | 1 | 0 | 0 | 0 | 
 |  |  |  |  |  |  |  |  |  | 1 | 0 | Remainder

## Slide 71: Example of Implementation 1
Let’s do 7 2
Iteration | Step | Quotient | Divisor | Remainder
0 | Initial values | 0000 | 0010 0000 | 0000 0111
1 | 1: Rem=Rem-Div | 0000 | 0010 0000 | 1110 0111
 | 2b: Rem<0=>+Div, sll Q, Q0=0 | 0000 | 0010 0000 | 0000 0111
 | 3: Shift Div right | 0000 | 0001 0000 | 0000 0111
2 | 1: Rem=Rem-Div | 0000 | 0001 0000 | 1111 0111
 | 2b: Rem<0=>+Div, sll Q, Q0=0 | 0000 | 0001 0000 | 0000 0111
 | 3: Shift Div right | 0000 | 0000 1000 | 0000 0111
3 | 1: Rem=Rem-Div | 0000 | 0000 1000 | 1111 1111
 | 2b: Rem<0=>+Div, sll Q, Q0=0 | 0000 | 0000 1000 | 0000 0111
 | 3: Shift Div right | 0000 | 0000 0100 | 0000 0111
4 | 1: Rem=Rem-Div | 0000 | 0000 0100 | 0000 0011
 | 2a: Rem≥0=> sll Q, Q0=1 | 0001 | 0000 0100 | 0000 0011
 | 3: Shift Div right | 0001 | 0000 0010 | 0000 0011
5 | 1: Rem=Rem-Div | 0001 | 0000 0010 | 0000 0001
 | 2a: Rem≥0=> sll Q, Q0=1 | 0011 | 0000 0010 | 0000 0001
 | 3: Shift Div right | 0011 | 0000 0001 | 0000 0001

## Slide 72: Division Improvements
Skip first subtract
  Can’t shift ‘1’ into quotient anyway
  Hence shift first, then subtract
    Undo extra shift at end
Hardware similar to multiplier
  Can store quotient in remainder register
  Only need 32-bit ALU
    Shift remainder left vs. divisor right

## Slide 73: Implementation 2
1. Place dividend in lower half
2. Do the division
3. Get remainder here
4. Get quotient here

## Slide 74: Implementation 2

## Slide 75: Restoring Division

## Slide 76: Further Improvements
Division still takes:
  2 ALU cycles per bit position
    1 to check for divisibility (subtract)
    One to restore (if needed)
Can reduce to 1 cycle per bit
  Called non-restoring division
  Avoids restore of remainder when test fails

## Slide 77: Non-Restoring Division
Consider remainder to be restored:
  Ri = 2 x Ri-1 – d < 0
  Since Ri is negative, we must restore it, right?
  Well, maybe not. Consider next step i+1:
  Ri+1 = 2 x (Ri) – d = 2 x (Ri – d) + d
Hence, we can compute Ri+1 by not restoring Ri, and adding d instead of subtracting d
  Same value for Ri+1 results
Throughput of 1 bit per cycle

## Slide 78: Non-Restoring Division
Iteration | Step | Divisor | Remainder
0 | Initial values | 0010 | 0000 0111
 | Shift rem left 1 | 0010 | 0000 1110
1 | 2: Rem = Rem - Div | 0010 | 1110 1110
 | 3b: Rem < 0 (add next), sll 0 | 0010 | 1101 1100
2 | 2: Rem = Rem + Div | 0010 | 1111 1100
 | 3b: Rem < 0 (add next), sll 0 | 0010 | 1111 1000
3 | 2: Rem = Rem + Div | 0010 | 0001 1000
 | 3a: Rem > 0 (sub next), sll 1 | 0010 | 0011 0001
4 | Rem = Rem – Div | 0010 | 0001 0001
 | Rem > 0 (sub next), sll 1 | 0010 | 0010 0011
 | Shift Rem right by 1 | 0010 | 0001 0011

## Slide 79: 4 x 4 Divider
A/B = Q + R/B
Algorithm:
R’ = 0
for i = N-1 to 0
R = {R’ << 1. Ai}
D = R - B
if D < 0, Qi=0, R’=R
else Qi=1, R’=D
R’=Rc

## Slide 80: What About Signed Division?
The simplest solution is to remember the signs of the divisor and dividend and then negate the quotient if the signs disagree.
However, (-7) 2 = ?
  (+7) (-2) = ?
  (-7) (-2) = ?
The correctly signed division algorithm negates the quotient if the signs of the operands are opposite and makes the sign of the nonzero remainder match the dividend.
Notes: The absolute value of quotient!
(+7) (-2) = -3 ...+1
(-7) (-2) = +3 ...-1
(+7) ÷ (-2) = -3 ...+1
(-7) ÷ (-2) = +3 ...-1